#### D3		WATER MANAGEMENT AREA 3: CROCODILE (WEST) AND MARICO

##### D3.1	Introduction

The Crocodile (West) and Marico water management area borders on Botswana to the north-west. Its main rivers, the Crocodile and Marico, give rise to the Limpopo River at their confluence. The climate is generally semi-arid, with the mean annual rainfall ranging from 400 mm to 800 mm. Extensive irrigation development occurs along the main rivers, with grain, livestock and game farming in other parts. A general orientation is given by Fig. D3.

Economic activity in the water management area is dominated by the urban and industrial complexes of northern Johannesburg and Pretoria and platinum mining north-east of Rustenburg. It is the second most populous water management area in the country and has the largest proportionate contribution to the national economy.

Development and utilisation of surface water occurring naturally in the water management area has reached its full potential. Large dolomitic groundwater aquifers occur along the southern part of the area, which is the reason for part of the Upper Molopo River catchment being incorporated into the area. The aquifers are utilised extensively for urban and irrigation purposes. Localised over-exploitation of groundwater occurs in the Molopo area. Some aquifers also underlie the border with Botswana and are shared with that country. A substantial portion of the water used in the water management area is transferred from the Vaal River and further afield. Small transfers out of the water management area are to Gabarone in Botswana and to Modimolle in the Limpopo water management area.

Increasing quantities of effluent return flow from urban and industrial areas offer considerable potential for re-use, but the effluent is at the same time a major cause of pollution in some rivers.

Population and economic growth, centred on the Johannesburg-Pretoria metropolitan complex and mining developments, are expected to continue strongly in this area. Little change is foreseen in population and economic development in rural areas.

Fig. D3: Base map of the Crocodile (West) and Marico water management area

D3.2	Key statistics relevant to the Crocodile (West) and Marico water management area

Tables D 3.1 to 3.6 contain a breakdown of the information given in Tables 2.1 to 2.6 of Chapter 2 for each sub-area of the Crocodile (West) and Marico water management area. The data is primarily derived from the standardised data base. Different information may be available from other sources.

Table D3.1:	Natural mean annual runoff (MAR) and ecological Reserve (million m³/a)

| Component/ Sub-area | Natural MAR1 | Ecological Reserve1, 2 |
| --- | --- | --- |
| Apies/Pienaars | 142 | 34 |
| Upper Crocodile | 253 | 57 |
| Elands | 113 | 15 |
| Lower Crocodile | 138 | 25 |
| Marico | 172 | 29 |
| Upper Molopo | 37 | 4 |
| Total for WMA | 855 | 164 |

- Quantities are incremental and refer only to the sub-area under consideration.

- The total volume is based on preliminary estimates, with the impact on yield being a portion of this.

Table D3.2:	Available water in year 2000 (million m³/a)

| Component/ Sub-area |  | Natural resource |  |  | Usable return flow |  | Total local yield |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Surface water1 | Ground-water | Irrigation | Urban | Mining and bulk |  |
| Apies/Pienaars | 38 | 36 | 4 | 106 | 2 | 186 |
| Upper Crocodile | 111 | 31 | 21 | 158 | 15 | 336 |
| Elands | 30 | 29 | 3 | 10 | 14 | 86 |
| Lower Crocodile | 7 | 29 | 14 | 1 | 8 | 59 |
| Marico | 14 | 12 | 2 | 3 | 1 | 32 |
| Upper Molopo | 3 | 9 | 0 | 5 | 2 | 19 |
| Total for WMA | 203 | 146 | 44 | 283 | 42 | 718 |

- After allowance for the impacts on yield of the ecological component of Reserve, river losses, alien vegetation, rain-fed sugar cane and urban runoff.

Table D3.3:	Year 2000 water requirements (million m³/a)

| Sector/ Sub-area | Irrigation | Urban1 | Rural1 | Mining and bulk industrial2 | Power generation3 | Affores- tation4 | Total local require-ments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Apies/Pienaars | 41 | 211 | 7 | 6 | 15 | 0 | 280 |
| Upper Crocodile | 208 | 292 | 5 | 38 | 13 | 0 | 556 |
| Elands | 32 | 23 | 10 | 48 | 0 | 0 | 113 |
| Lower Crocodile | 137 | 3 | 3 | 28 | 0 | 0 | 171 |
| Marico | 24 | 5 | 9 | 2 | 0 | 0 | 40 |
| Upper Molopo | 3 | 13 | 3 | 5 | 0 | 0 | 24 |
| Total for WMA | 445 | 547 | 37 | 127 | 28 | 0 | 1 184 |

- Includes Reserve component for basic human needs at 25 ℓ/c/d.

- Mining and bulk industrial water uses that are not part of urban systems.

- Includes water for thermal power generation only. (Water for hydropower, which represents a small portion of power generation in South Africa, is generally available for other uses as well.)

- Quantities refer to the impact on yield only.

Table D3.4: Reconciliation of water requirements and available water for year 2000 (million m³/a)

| Component/ Sub-area | Local Yield | Transfers in2 | Local requirements | Transfers out2 | Balance1 |
| --- | --- | --- | --- | --- | --- |
| Apies/Pienaars | 186 | 182 | 280 | 87 | 1 |
| Upper Crocodile | 336 | 279 | 556 | 17 | 42 |
| Elands | 86 | 71 | 113 | 24 | 20 |
| Lower Crocodile | 59 | 112 | 171 | 0 | 0 |
| Marico | 32 | 0 | 40 | 7 | ( 15) |
| Upper Molopo | 19 | 0 | 24 | 0 | ( 5) |
| Total for WMA | 718 | 519 | 1 184 | 10 | 43 |

- Brackets around numbers indicate a negative balance. Surpluses are shown in the most upstream sub-area where they first become available.

- Transfers into and out of sub-areas may include transfers between sub-areas as well as transfers between WMAs. The addition of the transfers per sub-area therefore does not necessarily correspond to the total of transfers into and out of the WMA. The same applies to Tables D3.5 and D3.6.

Table D3.5:	Reconciliation of water requirements and availability for the year 2025 base scenario (million m³/a)

| Component/ Sub-area | Local yield1 | Transfers in | Local requirements2 | Transfers out | Balance3 | Potential for develop- ment4 |
| --- | --- | --- | --- | --- | --- | --- |
| Apies/Pienaars | 244 | 287 | 399 | 92 | 40 | 0 |
| Upper Crocodile | 399 | 382 | 673 | 13 | 95 | 0 |
| Elands | 90 | 71 | 124 | 24 | 13 | 0 |
| Lower Crocodile | 59 | 113 | 173 | 0 | ( 1) | 0 |
| Marico | 32 | 0 | 40 | 7 | ( 15) | 0 |
| Upper Molopo | 22 | 0 | 29 | 0 | ( 7) | 0 |
| Total for WMA | 846 | 727 | 1 438 | 10 | 125 | 0 |

- Based on existing infrastructure and infrastructure under construction in the year 2000. Also includes return flows resulting from a growth in requirements. It is assumed that water will be transferred into Apies/Pienaars and Upper Crocodile sub-areas from the Upper Vaal water management area to meet the anticipated growth in requirements.

- Based on growth in water requirements as a result of population growth and general economic development. Assumes no general increase in irrigation.

- Brackets around numbers indicate negative balance.

- No significant potential for the further development of local resources.

Table D3.6: Reconciliation of water requirements and availability for the year 2025 high scenario (million m³/a)

| Component / Sub-area | Local yield1 | Transfers In | Local requirements2 | Transfers out | Balance3 | Potential for develop- ment4 |
| --- | --- | --- | --- | --- | --- | --- |
| Apies/Pienaars | 360 | 517 | 630 | 95 | 152 | 0 |
| Upper Crocodile | 511 | 584 | 880 | 13 | 202 | 0 |
| Elands | 97 | 71 | 141 | 24 | 3 | 0 |
| Lower Crocodile | 62 | 116 | 179 | 0 | ( 1) | 0 |
| Marico | 33 | 0 | 42 | 7 | ( 16) | 0 |
| Upper Molopo | 21 | 0 | 27 | 0 | ( 6) | 0 |
| Total for WMA | 1 084 | 1 159 | 1 899 | 10 | 334 | 0 |

- Based on existing infrastructure and infrastructure under construction in the year 2000 and includes return flows resulting from the growth in requirements. It is assumed that water to meet the anticipated growth in water requirements will be transferred into Apies/Pienaars and Upper Crocodile sub-areas from the Upper Vaal water management area.

- Based on growth in water requirements as a result of population growth and general economic development. Assumes no general increase in irrigation.

- Brackets around numbers indicate a negative balance.

- There is no significant potential for the further development of local resources.

D3.3	Key elements of the broad strategic perspectives for the Crocodile (West) and

Marico water management area

The key considerations for the Crocodile (West) and Marico water management area are that its own water resources are already fully utilised, the importance of transfers and return flows in the water balance, and the continued strong growth expectations in the Pretoria-Johannesburg and the Platinum Belt regions. Inherently these factors will impact on flows and water quality along the Crocodile River and also on South Africa's international obligations. Compared to the natural mean annual runoff of 855 million m3/a that originates in the water management area, an estimated 549 million m3/a still flows out of the area, 96 per cent to the Limpopo River.

Important considerations that will have to receive attention are the optimal use of return flows, the maintenance of an optimal balance between the urban re-use of return flows and transfers of water into the water management area, and water quality management. Water demand management, combined with the other options for the reconciliation of requirements and the availability of water, as described under Section 2.5, should receive due consideration. After that, growth in requirements in the Pretoria-Johannesburg area will mainly have to be supplied from transfers, while growth in the Elands and Lower Crocodile sub-areas can largely be supplied from increasing return flows. Much of the requirements of the ecological component of the Reserve can also be supplied from return flows, although intervention may be required to ensure the appropriate temporal distribution of flows.

The following reservations will apply with respect to the Crocodile (West) and Marico water management area:

- An additional 220 million m³/a will have to be transferred from the Upper Vaal and water management areas beyond to the Pretoria-Johannesburg area in future. As an upper high-growth scenario, up to 750 million m³/a may be required – reserved in the Upper Vaal water management area.

- Surplus effluent return flows that become available are to be reserved in the Crocodile (West) and Marico water management area for the following priorities:

- Re-use for urban, industrial and mining purposes where this will feasibly contribute to reducing transfers into the water management area.

- About 45 million m³/a may be required for developments in the Lephalale area in the Limpopo water management area. This quantity is not included in Tables D3.5 and D3.6.

- Small quantities may be required to augment supplies in the Limpopo and Olifants water management areas.

- The transfer of about 7 million m³/a from the Molatedi Dam to Gabarone in Botswana – reserved in the Crocodile (West) and Marico water management area.

- Continuation of small transfers from the Olifants to the Crocodile (West) and Marico water management area, as well as from the Crocodile (West) and Marico to the Limpopo water management area – reserved in the Olifants, and Crocodile (West) and Marico water management areas respectively.

- Water resource developments that may negatively influence the flow of water towards neighbouring countries will be subject to national authorisation – reservation with respect to Crocodile (West) and Marico water management area.