## Slide 1
PRESENTATION TITLE
Presented by:
Name Surname
Directorate
Date
Classification, Reserve & RQO determination of water resources in the Mvoti to Umzimkulu Water Management Area
GROUNDWATER RESOURCE QUALITY OBJECTIVES
K. Sami
WSM Leshika Consulting Engineers
16 August 2015

## Slide 2
Determining RQOs for Groundwater
Assessed groundwater using the previous Groundwater Reserve Investigation (SRK, 2014)
Detailed assessment of groundwater resources and contribution to baseflow – fully account for groundwater-surface interaction
Express groundwater use relative to resources and impacts on baseflow
Evaluate groundwater quality and Groundwater Quality Category
Express in terms of Present Class
Determine additional available groundwater resources with respect to the EWR low flow per catchment
Develop the RQOs

## Slide 3
Process
Domestic use
Irrigation use
Calibration vs
Recharge data
Gauging weirs
dams
DEVELOP RQO
Recharge
Stress index
Other uses
Climate data
Impact on baseflow
Input data
Groundwater quality
Modelling
Model Outputs
Calculations and classification
WRSM 2000 monthly model
Caclulate present status
Natural + present baseflow
Groundwater cycle
EWR
ALLOCATABLE GROUNDWATER
Borehole yields

## Slide 4: Study area IUAs
Grouped by:
Geology
Catchment
Topography

## Slide 5: Study area Geology

## Slide 6
  Demand - Aquifer Recharge
Class Use/ Aquifer recharge
F >95% Critically modified
E >65% Seriously modified
D >40% Largely modified
C >20% Moderately modified
B >5% Largely natural
A <5% Unmodified
How much groundwater is still available? Not much significant groundwater use

## Slide 7
  Water Quality Category
Water Quality Category
III
II
I
Water Quality issues in the Natal Metamorphic Province, especially Fluoride
III <75% DWS Class 0-1
II >95% DWS Class 2, or >75% 0-1
I >95% DWS Class 0-1

## Slide 8
  Baseflow Reduction
Baseflow reduction
F >95% Critically modified
E >65% Seriously modified
D >40% Largely modified
C >20% Moderately modified
B >5% Largely natural
A <5% Unmodified
Baseflow reduction due to Afforestation and sugar cane and AIPs significant in some areas

## Slide 9
  Parameters for Setting RQOs
Baseflow
Water Quality
Harvest Potential vs groundwater use
Water Level
  ParameRQOs

## Slide 10
  Priority Areas for Groundwater RQOs

## Slide 11
  GROUNDWATER UTILISATION