## Slide 1
FROM SCENARIOS TO MANAGEMENT CLASSES:
Water Resource System and
Modelling
Presented by: Pieter van Rooyen
26 November 2013

## Slide 2
Rural
Urban
Rural
Small Dams
Stream Flow Reduction
Industrial
Nature Reserve
Typical water resource system
Trout farming, recreation, dry-land agriculture
Forestry
Releases down river for irrigation, urban and industrial
Irrigation from canal
Rural: Subsistence, settlements
Gorge, protected area
Irrigation from river
Town supplied directly from large dam
Estuary
Treated wastewater
Large
Dam

## Slide 3: Water Resource Modelling
Apply available hydrological data and models.
Refine model configuration to reflect relevant elements influencing the water balance.
Disaggregate network to represent flow at all Ecological Water Requirement Sites.
Prepare monthly time series data Natural, Present Day and for alternative scenarios.
Summarize information of time series:
  Monthly distribution curves
  Dam spill event statistics

## Slide 4
Scenario description
SC | Description
A | Dam is raised and water released down river (canal obsolete). Increased irrigation to maximum potential. Waste water release in estuary increased. No EWR releases.
B | Status quo maintain but current waste water is re-used (i.e. decreased flow and better quality into estuary)
C | Dam is raised, canal and pipe enlarged so river not used as a conduit. Increased irrigation and increased waste water, but conveyed into marine system (sea outfall). EWRs are released for the REC but the low flows are decreased by 10%.
D | Dam is raised and existing canal system fixed. For the additional irrigation (cut to 30% from the maximum potential), the water is released downstream in the river, but with some seasonality built in. Increased waste water into estuary. EWR releases for REC but low flows decreased by 10%.

## Slide 5
 | DRIVERS |  |  | 
SCENARIOS | Dam raising | Increased irrigation | Increased waste water | EWR release
A |  Release down river |  |  | 
B |  |  | Re-use | 
C | ; enlarge pipe & canal |  | Sea outfall | -10% low flows
D | ; Use existing canal (fix problems) | -30%. Release additional water DS with EWR seasonality |  | -10% low flows
Scenario description: Matrix