## Slide 1
NON-ECOLOGICAL WATER QUALITY: CONSEQUENCES TO SCENARIOS
Presented by:
Patsy Scherman
Scherman Colloty & Associates
3 April 2014

## Slide 2
NWRCS INTEGRATED STEPS
1: Delineate units of analysis and describe the status quo
2: Initiation of stakeholder process and catchment visioning
3: Quantify EWRs and changes in Ecosystem Services
7: Gazette class configuration
4: Identification and evaluation of scenarios within IWRM
5: Draft Management Classes
6: Resource Quality Objectives (EcoSpecs & water quality (user))
Water quality consequences:
Where does it fit in?

## Slide 3
Water quality = two broad components
  Ecological, i.e. as part of the EWR or Reserve process. Scenario process + evaluation: standard process
  Non-ecological, i.e. UserSpecs (uses such as irrigation + stock-watering, domestic, recreation, industrial). Water quality is incorporated in the consequence assessment as:
    part of ECOLOGICAL consequences
    a service identified in ECOSYSTEM SERVICES
    indirectly in the ECONOMICS ito water treatment costs
    A 4th component, i.e. direct impact on NON-ECOLOGICAL WATER QUALITY
STEPS 4 - 6: WATER QUALITY

## Slide 4: APPROACH

## Slide 5: LETABA RIVER: DOWNSTREAM EBENEZER DAM
CS
Sc 5,6
9,10
Site location
Letaba River: Downstream Ebenezer to Tzaneen Dam. Reach includes EWR 1 (Appel)
Primary user
Forestry + limited agriculture
Primary wq driver
Nutrients
Current State
Good
Results
All scenarios slightly worse than CS

## Slide 6: LETSITELE RIVER
CS / Sc 9,10
Sc 4,5,6
Site location
Letsitele River. Reach includes EWR 2
Primary user
Citrus plantations + irrigation
Primary wq driver
Nutrients, salts, potential toxics
Current State
Fair - Moderate
Results
Sc9 and 10 same as CS.
Sc4,5,6 slightly better than CS.

## Slide 7: LETABA RIVER REACH INCLUDING EWR 3
CS / Sc 3,5,
6,9,10
Site location
Letaba River: B81F-00200, 00218, 00231. Reach includes EWR 3 (Prieska weir)
Primary user
Citrus plantations + irrigation
Primary wq driver
Nutrients, salts, potential toxics
Current State
Moderate - Good
Results
All scenarios maintain CS

## Slide 8: LETABA RIVER REACH INCLUDING EWR 4
CS / Sc 3,5,
6,10
Site location
Letaba River: B81J-00219. Reach includes EWR 4 (Letaba Ranch)
Primary user
Settlements; irrigation
Primary wq driver
Nutrients, turbidity (from erosion)
Sc 9
Current State
Moderate - Good
Results
Sc9 slightly better than CS.
All other scenarios maintain CS.

## Slide 9: KLEIN LETABA RIVER
Sc 5,6
9,10
Site location
Klein Letaba River: B82G-00135. Reach includes EWR 5
Primary user
Settlements; subsistence farming;
urban area
Primary wq driver
Nutrients, salt, turbidity
CS
Current State
Moderate - Good
Results
All scenarios slightly worse than CS

## Slide 10: LETABA RIVER: KRUGER NATIONAL PARK (EWR 7)
CS / Sc 10
Site location
Letaba River: B83D-00255, KNP.
Reach including EWR 7
Primary user
National Park so conservation +
biodiversity
Primary wq driver
Nutrients, salt, turbidity
Sc 3,5,6,9
Current State
Good
Results
Sc10 maintains CS.
All other scenarios slightly worse than CS.

## Slide 11: CONCLUSIONS
Ranking of scenarios per RU not undertaken due to:
  small differences in impact of scenarios
  lack of resolution to differentiate between scenarios for the various sites
Water quality state remains generally Good under all scenarios
Little impact is expected under any of the operational scenarios for identified non-ecological water quality users