## Slide 1: CLASSIFICATION OF SIGNIFICANT WATER RESOURCES AND DETERMINATION OF RESOURCE QUALITY OBJECTIVES FOR WATER RESOURCES IN THE USUTU TO MHLATHUZE CATCHMENTS (WP11387)
Project Steering Committee 1, Virtual: 7 June 2022

## Slide 2
8.1.2 & 8.1.3 RIVER STATUS QUO & IUA DELINEATION
Delana Louw
Rivers for Africa

## Slide 3
DELINEATION AND INTEGRATED UNITS OF ANALYSIS
To understand what IUAs are and why delineation is required, i.e., the context, we need to remind ourselves of the basics.
What is Classification?
Balance between
Protection
(Ecology)
Use
Expressed as Ecological state
includes Water balance, quality, socio-economics
&

## Slide 4
CLASSES | DESCRIPTION
I | Ecology: Mostly in good condition Use: Minimal
II | Ecology: Mostly in moderate condition Use: Medium
III | Ecology: Mostly in poor condition Use: High – work horse river.
Use
Ecology
How is Classification described?
DELINEATION AND INTEGRATED UNITS OF ANALYSIS (cont.)

## Slide 5
{
Close to Natural: Good condition
Very different to Natural: Very Poor condition
{
Ecological Categories (EC)
DELINEATION AND INTEGRATED UNITS OF ANALYSIS (cont.)

## Slide 6
What scale do we classify at?
Classify every Integrated Unit of Analysis. Units are similar ito land use &/or ecological state. Very simply put, an IUA consist of many river reaches, wetlands and/or estuaries.
Provide the Catchment Configuration for every IUA. (Provide the ecological state for each of the river reaches and estuaries, (described as Resource Units (RU) that are within the IUA).
DELINEATION AND INTEGRATED UNITS OF ANALYSIS (cont.)

## Slide 7
IUA: Homogenous area that can be managed as an entity.
River RESOURCE UNITS: RUs require different EWRS (due to different flow patterns, reaction of habitat and biota to stress, management and operational structures). RUs have been delineated based on similarity of ecological state and the causes and sources (impacts).
NOTE
IUAs and RUs are both homogenous catchments. However, the scale is different and RUs are nested within IUAs.
IUA AND CATCHMENT CONFIGURATION DEFINITIONS

## Slide 8
BIOPHYSICAL NODES: A point in the river which can be a survey site or a hypothetical point (‘site’). These are points which are used to assess the Ecological Water Requirements (EWRs).
NODES, RUS, IUAS – REPRESENT A CATCHMENT CONFIGURATION WHICH WILL DEFINE OR UNPACK THE CLASS FOR A SPECIFIC IUA
IUA and catchment configuration definitions (cont.)

## Slide 9: DELINEATION PROCESS
  PES have been determined for every SQ during 2014 and reviewed now during this study.
  According to similar ecological state, and land use (impacts), SQ catchments have been grouped into RUs.
  Using the PES for the SQs, a PES was assigned to the RUs.
  Using Socio-economics (economics and ecosystem services), water resource and infrastructure, and water quality information, RUs were grouped into IUAs to ensure that it represents a homogenous area that can be managed as an entity.

## Slide 10: PROPOSED IUAs FOR W PRIMARY CATCHMENT

## Slide 11: PRELIMINARY IUAs FOR W PRIMARY CATCHMENT (cont.)

## Slide 12: RIVER ECOLOGICAL STATUS
Each Secondary Catchment (W1 – W7) will be presented.
The Secondary Catchment is divided into RUs (grey border).
Each RU is colour filled with the colour associated with the PES.
Red lines show the IUAs. They are labelled in boxes and info is provided regarding reasons for the allocated PES (status quo).
Areas shaded white is associated with the estuaries within the IUA.
The estuary PES will be provided during a following presentation.
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 13: W1 (Mhlathuze): Status quo
IUA W12-a_(Upper Mhlathuze). Roads, extensive overgrazing, sand mining, alien vegetation, forestry, small dams Largely PES C
IUA W11 (Matigulu). Extensive agriculture, veg clearing, alien veg. Largely PES C
IUA W13 (Mlalazi). Largely PES C apart from section in Reserve. Sugarcane, urban.
IUA W12-b_(Mfule, Mhlatuzane, Nseleni).
IUA W12-c (Lower Mhlathuze).
Tribs dominated by rural settlements, forestry, dams, towns. Mhlathuze river has changed in character (alluvial to pool rapid, canalised and levees in lower section. Largely PES C
IUA W12-d (Nhlabane)
IUA W12-e (Msingazi)
Extensive forestry, storm water, RMB smelter, urban. Largely EPS C.
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 14: W2 (Umfolozi): Status quo
IUA W23 (Upper Umfolozi incl Lower White & Black Umfolozi)
In and downstream iMfolozi Game Reserve – B PES
IUA W21 (Upper & Middle White Umfolozi).
IUA W22_(Upper Black Umfolozi).
Outside Game Reserve: Forestry, dams, irrigation, erosion, sedimentation. Largely C.
Bordering or in Game Reserve: Largely B PES
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 15: W3 (Mkuze): Status quo
IUA W31-a (Upper Mkuze)
Forestry, coal mining, instream dams, rural areas, irrigated crops, alien vegetation erosion, sedimentation– C - B PES.
IUA W31-b (Lower Mkuze)
C outside Mkuze Game Park, B PES within or border.
IUA W32-a (Upper Hluhluwe).
Hluhluwe Game Reserve.
Largely B PES
IUA W32-b (Nyalezi & Mzinene)
Sand mining, overgrazing, subsistence farming, erosion, sugarcane, urban, instream dams, levees. Largely C PES.
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 16: W4 (Pongola): Status quo
IUA W41 (Bivane)
Forestry, agriculture.
Largely C PES.
IUA W42-a (Upper Pongola)
Forestry, agriculture, Paul Pietersburg water quality issues.
C PES
IUA W42-b (Middle Pongola, Ithala).
Instream dams, forestry, agriculture, alien veg, overgrazing, sand mining (C PES). Ithala – B PES
IUA W44 (Middle Pongola)
Impala Irrigation Board – canal system, Grootdraai Weir, flow regulation. D PES.
IUA W45 (Lower Pongola Floodplain)
Flow changes, subsistence agriculture, forestry, sedimentation.
C PES.
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 17: W5 (Usutu): Status quo
IUA W51 (W5 Upstream Major Dams)
Forestry, alien veg, agriculture.
C - D PES
IUA W53 (Mpuluzi & Lusushwana).
Small dams, forestry, agriculture, subsistence farming (B/C - C PES).
IUA W57 (Lower Usutu)
Borders Ndumo Game Reserve. B/C PES.
IUA W52 (W5 Downstream major dams and Hlelo)
Upstream dams and flow changes, forestry, alien veg agriculture, mining.
Largely C PES.
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify

## Slide 18: W7 (Kosi & Sibaya): Status quo
IUA W70-b (Sibaya).
Water quality impacts from township and hospital.
D PES.
IUA W70-a (Kosi)
B PES in Isimangaliso Wetland Park and C PES outside (urban areas, WWRW, forestry).
Notes: Caryn to do the scope, will be Tasks of study, deliverables, reference to previous ewr study, use some of following slides, but simplify