## Slide 1
PRESENTATION TITLE
Presented by:
Name Surname
Directorate
Date
Support of the Water Reconciliation Strategy for the Algoa Water Supply System
ATSG Meeting
Aurecon
15 August 2018

## Slide 2
Feasibility evaluation: Additional balancing storage in the LSRGWS

## Slide 3: Balancing Dam Options
Following preliminary screening, costing and comparison:
Construction of a 4.6 million m3 balancing dam near present Scheepersvlakte Dam & integration with existing gravity pipeline to Nooitgedagt WTW:
Lower Coerney Dam
Upper Scheepersvlakte Dam

## Slide 4: Construction of a larger dam near the present Scheepersvlakte Dam site
Both sites falls on land being planned for development by the Scheepersvlakte 98 Citrus Development Trust
The Trust agreed to co-operate with the DWS and possible future works, should the new dam option be pursued further
The dam will be sized for the combined NMBM balancing capacity of 4 410 Mℓ (21 days balancing storage) plus the Developer’s required irrigation capacity (~ 180 Mℓ, one week of storage)

## Slide 5: Scheepersvlakte Farm & dam locations

## Slide 6
  Lower Coerney Dam

## Slide 7: Next Steps
Draft EIA scope of work provided with notes
Detailed geotechnical evaluation to assess suitability of short-listed dam sites is underway:
  Geophysical survey – complete
  Test pitting – mostly complete (access constraints)
  Rotary core drilling – establish week of 20 Aug
  Lab testing – initial analysis done
  Data analysis, interpretation and reporting
Topographical site survey of selected dam site done:
  Done by DWS NWRI survey team
  Small additions to be surveyed for pipework area
Flood assessment for Lower Coerney Dam
Reserve determination for Lower Coerney Dam

## Slide 8
WUE assessment - Fish and Sundays catchments

## Slide 9: Project objectives
Algoa Recon Strategy Support: To put in place arrangements and resources for ongoing implementation of the recommendations and maintenance of the Algoa Reconciliation Strategy.
Evaluation of Water Use and Allocation in the OFS System: To evaluate the efficiency of the Eastern Cape Province Orange River Project.
Additional Balancing Storage for NMBM: To remove potential operating system constraints for sustainable delivery of bulk Orange River water supply to the Lower Sundays River Government Water Scheme (LSRGWS) and to Nelson Mandela Bay Municipality (NMBM), for water requirements up to 2040.

## Slide 10: Recommended WUE Savings
Recommended Intervention | Potential Water Savings (million m3/a)
Reduce allowance for canal losses in the GFRWUA (incl. clearing of vegetation along canals & lining of “hot spot” priority canal sections) | 40
Reduced operational releases at Elandsdrift & De Mistkraal Weirs | 31
Rehabilitation of Darlington Dam & reducing spills at Korhaansdrift Weir | 18
Improve measuring and monitoring systems | Not quantified
Estimated savings: | 89 million m3/a
Notes: Final recommendations will be made for the reallocation of the potential water savings in the Alternative Reallocation Options sub-report.

## Slide 11
No savings foreseen from WC/WDM at small towns or diversion at Hermanuskraal Weir to Makana LM & Tyhefu Irrigation Scheme
Avoid future under-utilisation of water from emerging farmers allocations, by learning from proven, sustainable emerging-farmer developments, to ensure the best possible chance of success
Phased implementation of recommended WUE interventions
Continuously monitor actual water savings realized & adjust savings targets
Conclusions

## Slide 12: Distribution of targeted savings
Proposed distribution of saved water | 2040 Target (million m3/a)
Reduced Orange River transfer volume to Eastern Cape | 64
Small towns to apply for further allocations | 7
NMBM to apply for further allocations | 18
Total | 89
Notes: Final recommendations will be made for the reallocation of the potential water savings in the Alternative Reallocation Options sub-report.

## Slide 13
Comparison of operational releases at Elandsdrift Weir
2017/18
: Great Fish River
55 million m3 less
OFS Real-time Model
2016/17

## Slide 14
AWSS Status Report

## Slide 15
Presentation Content
Water availability and requirements
Interventions
Scenario planning

## Slide 16
Water Availability

## Slide 17
Priority classes for different category water users
It is preferable that all irrigators receive the same priority water throughout the AWSS
Category | % of total water requirement allocated to indicated priority class and acceptable risk of non-supply (assurance of supply) |  |  | 
 | 1: 100(1) year (99%) | 1: 50 year (98%) | 1: 10 year (90%) | 1: 5 year (80%)
Irrigation Gamtoos | 30 | 20 | 20 | 30
Irrigation Other | 20 | 20 | 20 | 40
Urban | 50 | 20 | 20 | 10
Losses | 100 | 0 | 0 | 0
Environmental | 100 | 0 | 0 | 0

## Slide 18
Groundwater
Groundwater intervention | Lower estimate (million m3/a) | Upper estimate (million m3/a) | Assumed yield (million m3/a)
Coega Fault | 6 | 8 | 8
Churchill Dam | 2 | 4 | 3
Moregrove Fault | 0.8 | 1.6 | 1
Bushy Park | 2 | 4 | 4
Jeffreys Arch | 6 | 9 | 7
Van Stadens | 4 | 4 | 4
Gamtoos Valley | 2 | 4 | 3
Kruisrivier | 0.4 | 1 | 0.5
Total | 23.2 | 35.6 | 30.5
Summary of potential groundwater yields used in strategy

## Slide 19
Groundwater
Estimated borehole yields for NMBM from currently-planned boreholes
Area | Aquifer | Production boreholes | Mℓ/day | million m3/a
Wellfields |  |  |  | 
Coega Kop | Coega Fault - TMG | 5 | 13.0 | 4.7
Uitenhage | Coega Fault -TMG | 4 | 5.2 | 1.9
Churchill Dam (NMBM property) | Folded TMG | 12 | 5.2 | 1.9
Bushy Park (West) | TMG | 12 | 5.2 | 1.9
Moregrove | Moregrove Fault - TMG | 21 | 9.1 | 3.3
Total wellfields |  | 60 | 37.6 | 13.7
Individual boreholes |  |  |  | 
Individual Boreholes | Mostly TMG | 102 | 13.2 | 4.8
Total wellfields & individual Bhs |  | 162 | 50.8 | 18.5
Churchill Dam (CHD Pipeline) | Folded TMG | 6 | 4.1 | 1.5
Potential Total |  | 168 | 55 | 20

## Slide 20
Groundwater
Kouga Municipality – potential yields of recently drilled production boreholes
Town | Existing sources | Newly drilled production boreholes | Ml/day | million m3/a
Oyster Bay | Boreholes & springs | 2 | 0.2 | 0.06
Jeffreys Bay | Dams & boreholes | 2 | 0.8 | 0.30
Humansdorp | Dams, springs & boreholes | 2 | 0.8 | 0.30
Hankey | Dam | 1 | 0.9 | 0.31
Patensie/ Andrieskraal | Dam | 4 | 0.4 | 0.14
Total |  |  | 3.1 | 1.11

## Slide 21
Yield at 1:50 yr assurance of supply
Transferred Orange River water: yield increased following completion of Phase 2 of the Nooitgedagt Low Level Scheme, from 32.9 million m3/a (90 Ml/d) to 50.0 million m3/a (137 Ml/d)
Low confidence in the yields of the Kromme & Kouga sub-systems sub-system to be addressed in the Kouga-Kromme WAAS once the V&V study is complete
No change in yield of the Algoa WSS from 2017 analysis
Emergency drought infrastructure upgrades to NCLLS not considered
Algoa WSS water availability

## Slide 22
Long-term stochastic yields of the Algoa WSS:
Water supply from the Algoa WSS
Sources of supply | 1 in 50 year yield or existing allocation/use | 
 | (million m3/a) | (Ml/d)
NMBM older dams | 3.4 | 9.3
Groendal Dam | 6.8 | 18.6
Uitenhage Springs and boreholes | 2.2 | 6.0
Churchill/Impofu dams | 30.0 | 82.2
Kouga/Loerie dams | 75.0 | 205.5
Sundays River GWS transfer | 50.0* | 137
Combined Total Yield | 167.4 | 458.6
* Excludes interim yield achieved through emergency drought infrastructure added

## Slide 23
Water Use, Requirements and Balance

## Slide 24
Historical Use from the Algoa WSS
% linear growth pa 1.3%
Trendline growth pa 2.3%

## Slide 25
Historical Use from the Algoa WSS
Drought year

## Slide 26
2017/18 Use from the Algoa WSS
TOTAL 139.1 million m3/a

## Slide 27
2017/18 Use from the Algoa WSS
million m3/a
NMBM | Kouga LM | Hankie & Patensie | GIB | Groendal irrigation | Impofu Dam irrigation | Canal losses | TOTAL USE
97.8 | 5.38 | 1.1 | 23.6 | 2.4 | 2.0 | 6.2 | 139.1
Allocation of 4.5 million m3/a
Plus Coega SEZ potable use of 0.7 million m3/a

## Slide 28
Historical NMBM Average Daily Use

## Slide 29
Water Use Conclusions
The 2017/18 water use was severely restricted because of the drought
Gamtoos IB was especially negatively affected
Coega SEZ potable use still very low. No industrial water use
Water use exceeded allocations for Kouga LM
More severe restrictions to be implemented

## Slide 30
Future Water Requirements

## Slide 31
Water Requirement Scenarios
7 Water Requirement Scenarios developed - combinations of:
  Low growth of 1% compound growth
  Historical long-term growth of 2.3%
  High growth of 3.5% linear growth
  Coega IDP domestic & industrial water projections
  For Kouga LM linear growth of 3.3% high-growth used to be in line with DWS growth estimations
  Implementation of the Reserve
  Climate change
Base year value used for projections is theoretical, to avoid under-estimation of interventions required

## Slide 32
Coega IDZ Water Requirements

## Slide 33
Base year value for Scenarios
2017/18 historical water use value NOT used as starting point for scenario planning, because:
  2017/18 historical value reflects restricted use of the Algoa WSS during a significant drought
  Using this value as the starting point for scenario planning will lead to under-estimation of the interventions needed to ensure a long-term water balance
  Water use typically returns to pre-drought levels within a year or two, unless some drought WC/WDM measures are kept in place
Theoretical starting value corresponding closely with trendline value of historical use used for scenario projections
  2017/18 actual (restricted use) was 139.1 million m3/a
  2017/18 Scenario starting value is 169.4 million m3/a

## Slide 34
Influence of starting value on Scenario Planning
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Kouga dam replacement / raising
Desal – Marina Sea Salt
NLLS Phase 5
Theoretical starting value 2017/18
Actual 2017/18 use
Difference in future water demand to plan for at linear growth
4 less schemes identified

## Slide 35
Interventions

## Slide 36
Interventions Considered for Scenario Planning
WC/WDM: 5%, 10% & 15% savings
Nooitgedagt-Coega Low Level Scheme: Phases 3, 4 & 5
Effluent treated to industrial and/or potable standards
  Fish Water Flats WWTW Reuse, phased
  Coega WWTW Reuse, phased
Coega Kop & various other groundwater schemes
Lower Sundays River return flows
Seawater Desalination: Marina Sea Salt, NMBM (phased)
Raising of Kouga Dam / Guernakop Dam

## Slide 37
Changes to Interventions
Further allocation of Orange River water to NMBM
  NLLS Phase 4 – DWS has confirmed in-principle approval for NMBM to apply for additional 18.25 million m3/a (50 Ml/d), based on savings from WUE efficiency measures introduced in Great Fish & Sundays catchments - equivalent to difference between average flow and peak flow of the NCLLS Phase 3, i.e. 210 – 160 = 50 Mℓ/day.
  NLLS Phase 5 added – assumed further allocation from savings achieved, of 18.25 million m3/a (50 Mℓ/d), but this depends on the actual efficiency savings to be achieved

## Slide 38
Scenario Planning

## Slide 39
Scenarios Developed
Coega Industrial Water Requirements
Low Growth including Coega Potable: 1% compound growth + Coega potable
2.3% Growth including Coega Potable without WC/WDM
High Growth Potable (Reference): 3.5% linear growth + Coega potable
High Growth Potable without WC/WDM: 3.5% linear growth + Coega potable (no efficiency saving from WC/WDM)
High Growth including Coega: 3.5% linear growth + Coega potable and industrial
Worst Case: 3.5% linear growth + Coega potable and industrial, with climate change & implementation of the Reserve
Scenario Planning up to 2043

## Slide 40
1. Coega Industrial Water Requirements
Coega WWTW Industrial Reuse Ph 2 Ind
Coega WWTW Industrial Reuse Ph 2 pot
Coega WWTW Industrial Reuse Phase 3 pot
Coega WWTW Industrial Reuse Ph 4 Ind
FWF WWTW Industrial Reuse Ph 2
FWF WWTW Industrial Reuse Ph 1
Coega Industrial water requirements
Coega WWTW Industrial Reuse Ph 3 ind
Coega WWTW Industrial Reuse Ph 1 pot

## Slide 41
2. Low Growth including Coega Potable
Requirement = 1% compound growth + Coega potable
15% WC/WDM
15% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
3 groundwater schemes

## Slide 42
3. 2.3% Historical growth w/o WC/WDM
Requirement = 3.5% linear growth + Coega potable
15% WC/WDM
15% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
Desal – Marina Sea Salt
3 groundwater schemes
2 groundwater schemes
NLLS Phase 5

## Slide 43
4. High Growth Potable Scenario (Reference)
Requirement = 3.5% linear growth + Coega potable
15% WC/WDM
15% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
Desal – Marina Sea Salt
5 groundwater schemes
Seawater Desal Ph 1
Groundwater scheme
NLLS Phase 5
Seawater Desal Ph 2

## Slide 44
5. High Growth Potable without WC/WDM
Requirement = 3.5% linear growth + Coega potable
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Kouga dam replacement / raising
Desal – Marina Sea Salt
NLLS Phase 5

## Slide 45
6. High Growth including Coega (pot & ind)
Reuse Coega – ex FWF WWTW
15% WC/WDM
15% WC/WDM
Requirement = 3.5% linear growth + Coega pot & ind
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
Reuse Coega – Coega WWTW
Desal – Marina Sea Salt
4 Groundwater schemes
Groundwater scheme
NLLS Phase 5
Reuse Coega – ex Coega WWTW
Desal Phase 1
Desal Phase 2

## Slide 46
7. Worst Case Scenario
Reuse Coega – ex FWF WWTW
15% WC/WDM
15% WC/WDM
Requirement = 3.5% linear growth + Coega pot & ind
Reuse Coega – ex Coega WWTW
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Seawater Desal Ph 3
Desal – Marina Sea Salt
Kouga dam replacement / raising
Reuse Coega – ex Coega WWTW
NLLS Phase 5

## Slide 47
Scenario Conclusions
Current shortages caused by drought
Delayed funding of infrastructure, procurement and implementation leads to risks of not meeting water requirements
Water efficiency measures and behaviour should be made more permanent
Effective WC/WDM essential for NMBM & Kouga LM
Complete NLLS Ph3 & remove bottlenecks in delivery
Planning of interventions should proceed due to long implementation lead times & uncertainty in terms of growth in water requirements
Groundwater schemes to be pursued by NMBM & Kouga LM (also forms part of drought actions)
Kouga LM likely to be become more self-sufficient

## Slide 48: - Thank you -