## Slide 1
PRESENTATION TITLE
Presented by:
Name Surname
Directorate
Date
Support of the Water Reconciliation Strategy for the Algoa Water Supply System
SSC Meeting
Aurecon
27 September 2017

## Slide 2
8.2 Feasibility evaluation: Additional balancing storage in the LSRGWS

## Slide 3: Selected Options for Investigation
Construction of a larger dam near the present Scheepersvlakte Dam site and integrate this dam with the existing gravity pipeline to the Nooitgedagt WTW.
Construct a large balancing dam on the right bank near the Nooitgedagt WTW.

## Slide 4: Construction of a larger dam near the present Scheepersvlakte Dam site
The site falls on land being planned for development by the Scheepersvlakte 98 Citrus Development Trust.
The Trust agreed to co-operate with the DWS and possible future works, should the new dam option be pursued further.
The dam will be sized for the combined NMBM balancing capacity of 4 410 Mℓ (21 days balancing storage) plus the Developer’s required irrigation capacity.
Advantages | Disadvantages
Reduced risk of supply to NMBM Simplified operations for the LSRWUA Shared cost with Developer Simplified integration into existing system (close to ScD) | Shared with Developer = coordination needed Potential increase in quantum of algae Potential compensation for land Still reliant of existing pipeline = does not improve risk of failure

## Slide 5: Construction of a larger dam near the present Scheepersvlakte Dam site

## Slide 6: Construct a large balancing dam on the right bank near the Nooitgedagt WTW
The proposed dam would supply the Nooitgedagt WTW by gravity although it may be necessary to pump water into the dam.
Dam capacity – about 3.2 million m3/a.
The majority of the proposed site for the dam and reservoir is situated on private property which is currently utilised for game farming.
Advantages | Disadvantages
NMBM fully responsible for managing dam Simplified operations for the LSRWUA Reduced risk of supply to NMBM – close proximity to WTW | Added retention time = potential WQ issues Potential environmental impacts – loss of 60 ha vegetation Increased evaporation losses (of about 0.5 million m3/a)

## Slide 7: Construct a large balancing dam on the right bank near the Nooitgedagt WTW
Nooitgedagt WTW
Approximate Extent of Mudstone (T-Qg)
Approximate Extent of Proposed Dam
250 m

## Slide 8: Next Steps
Preliminary environmental investigation showed no “fatal flaws” for either option:
  but may need to revisit should sites change
Meet with respective land owners for both dam sites:
  Meeting & site visit on 9/10 Oct planned
  Discuss with Scheepersvlakte 98 Citrus Development Trust regarding their request for the temporary abstracting from Scheepersvlakte Dam
Detailed geotechnical study to assess suitability of short-listed dam sites
Then topographical site survey of selected dam site in support of preliminary design and costing to be done:
  To be undertaken by DWS NWRI survey team

## Slide 9
9.4 WUE assessment - Fish and Sundays catchments

## Slide 10: Short-listed WUE Interventions
Lining of earth canals in the GFRWUA
Improved measuring and monitoring
Clearing of reeds along the Great Fish River
Reduced operational releases at Elandsdrift Weir
Rehabilitation of Darlington Dam

## Slide 11: Preliminary Recommendations
Concrete lining of canals:
The lining of the 500 km of earth canals in the GFRWUA (Intervention 1) is not recommended to be considered further, as the URV for this intervention is too high.
Clearing of vegetation along canals is recommended.
The lining of prioritised “hot spot” high-loss canal sections may be a more feasible option as this will potentially lead to large volumes of water savings at a lower cost. It is recommended that this sub-intervention be investigated in more detail. A pilot test case may be useful to ascertain actual costs and to test this sub-option.

## Slide 12: Preliminary Recommendations
Improved measuring and monitoring:
The recommendations made for improved measuring and monitoring (Intervention 2) should be considered by the GFRWUA, LSRWUA and the DWS.
Although the potential water savings are not easily quantifiable at present, this intervention will lead to improved management of the system and improved compliance to water allocations and water requests made.
Notes: Installing real-time monitoring at existing DWS off-take measuring points to get real-time data to WUA without 6 – 8 week delay.
Install more measuring devices along the Great Fish River and main irrigation canals.
Measure flows at tail-end of canals to provide a comprehensive measure of total water use and return flows.

## Slide 13: Preliminary Recommendations
Removal of reeds:
The removal of reeds along the Great Fish River (Intervention 3) not be considered further.
Estimated potential water savings are very low in comparison to the other interventions.
Removal of reeds may lead to unintended environmental consequences.

## Slide 14: Preliminary Recommendations
Operational releases:
A reduction in operational releases made at Elandsdrift and De Mistkraal weirs (Intervention 4) should be implemented in a step-wise manner.
The reduction of operational releases at Elandsdrift and De Mistkraal weirs could reduce operational losses in the lower Fish River and result in a potential water saving of a maximum of 33 million m3/a, if the operational loss is halved.
This intervention has a low capital cost as it does not involve construction of water supply infrastructure.

## Slide 15: Preliminary Recommendations
Refurbishment of Darlington Dam:
The refurbishment of the Darlington Dam (Intervention 5) is currently being evaluated by the DWS. The refurbishment of Darlington Dam could result in water savings in the lower Sundays River catchment due to reduced spills at Korhaansdrift Weir.
Additional yield will also be created should additional allocations be made to the NMBM.
This may influence the potential Lower Sundays River Return Flows Scheme

## Slide 16: Summary of Potential Savings
Recommended Intervention | Potential Water Savings (million m3/a)
Reduced operational losses at Elandsdrift Weir | Maximum of 33 – will be less than this in practise
Clearing of vegetation along GFRWUA earth canals | 4
Lining of “hot spot” priority canal sections in the GFRWUA | Not quantified – needs further investigation
Rehabilitation of Darlington Dam | Could save up to 18 by reducing spills at Korhaansdrift Raising of dam could lead to additional HFY to NMBM of max 10
Estimated total potential savings: | 15 – 30 million m3/a
Notes: Final recommendations will be made for the reallocation of the potential water savings in the Alternative Reallocation Options sub-report.

## Slide 17
12.2 Potential future Orange River water allocations

## Slide 18: Potential additional Orange River water allocations
The water savings which could potentially be reallocated to the NMBM, should all of the final recommended WUE options be successfully implemented, may amount to 18 million m3/a (50 Mℓ/day)
  Phasing may be needed
  Preliminary recommendation
  Allocations may need to be subject to WUE savings
This is equivalent to the difference between the average flow and peak flow of the Nooitgedagt Low-Level Scheme Phase 3, i.e. 210 – 160 = 50 Mℓ/day.

## Slide 19: Design Water Requirements
This is a preliminary recommendation for a potential reallocation volume to the NMBM, and it is possible that the actual volume that can potentially be reallocated may be lower or higher than these estimates.
It is recommended that a conservative approach be taken for the preliminary sizing of any potential future bulk water supply or storage infrastructure designed as part of this study, which can be refined once the potential savings are better understood.
Notes: The capacity of the delivery bulk pipeline from Scheepersvlakte Balancing Dam to the Nooitgedagt WTW is 102.2 million m3/a (280 Mℓ/day), and this is a realistic estimate to consider as the upper limit of the potential WUE water savings at this stage. For the transfer of water volumes higher than this capacity, a new pipeline would need to be constructed to the WTW. This pipeline capacity is 25.6 million m3/a (70 Mℓ/day) more than the peak capacity of Phase 3 of the Nooitgedagt Low-Level Scheme.

## Slide 20
AWSS Status Report

## Slide 21
Presentation Content
Water availability and requirements
Interventions
Scenario planning

## Slide 22
Water Availability

## Slide 23
Priority classes for different category water users
Algoa Operating Analysis 2017 noted that it is preferable that all irrigators receive the same priority water throughout the AWSS (to be addressed in future AOAs)
Category | % of total water requirement allocated to indicated priority class and acceptable risk of non-supply (assurance of supply) |  |  | 
 | 1: 100(1) year (99%) | 1: 50 year (98%) | 1: 10 year (90%) | 1: 5 year (80%)
Irrigation Gamtoos | 30 | 20 | 20 | 30
Irrigation Other | 20 | 20 | 20 | 40
Urban | 50 | 20 | 20 | 10
Losses | 100 | 0 | 0 | 0
Environmental | 100 | 0 | 0 | 0

## Slide 24
Groundwater
Groundwater intervention | Lower estimate (million m3/a) | Upper estimate (million m3/a) | Assumed yield (million m3/a)
Coega Fault | 6 | 8 | 8
Churchill Dam | 2 | 4 | 3
Moregrove Fault | 0.8 | 1.6 | 1
Bushy Park | 2 | 4 | 4
Jeffreys Arch | 6 | 9 | 7
Van Stadens | 4 | 4 | 4
Gamtoos Valley | 2 | 4 | 3
Kruisrivier | 0.4 | 1 | 0.5
Total | 23.2 | 35.6 | 30.5
Summary of potential groundwater yields:

## Slide 25
Transferred Orange River water: yield increased following completion of Phase 2 of the Nooitgedagt Low Level Scheme, from 32.9 million m3/a (90 Ml/d) to 50.0 million m3/a (137 Ml/d)
Yield of the Kromme sub-system was reduced from 43 (long-term yield) to 30 (firm yield) million m3/a, to be in line with the Algoa Operating Analysis (historical yield also adjusted to account for this)
  This change has significant long-term planning implications
It is evident that the yield of the Kouga/Loerie sub-system is too high. To be addressed in the Kouga-Kromme WAAS once the V&V study is complete
Algoa WSS water availability

## Slide 26
Long-term stochastic yields of the Algoa WSS:
Water supply from the Algoa WSS
Sources of supply | 1 in 50 year yield or existing allocation/use | 
 | (million m3/a) | (Ml/d)
NMBM older dams | 3.4 | 9.3
Groendal Dam | 6.8 | 18.6
Uitenhage Springs and boreholes | 2.2 | 6.0
Churchill/Impofu dams | 30.0* | 82.2
Kouga/Loerie dams | 75.0 | 205.5
Sundays River GWS transfer | 50.0 | 137
Combined Total Yield | 167.4 | 458.6
* Also adapted for historical yield

## Slide 27
Water Use, Requirements and Balance

## Slide 28
Historical Use from the Algoa WSS
Chart: AWSS Total Annual Historical Use (million m3/a)
| 99/00 | 00/01 | 01/02 | 02/03 | 03/04 | 04/05 | 05/06 | 06/07 | 07/08 | 08/09 | 09/10 | 10/11 | 11/12 | 12/13 | 13/14 | 14/15 | 15/16
 | 112.482 | 132.8479 | 136.883 | 136.996 | 141.3603 | 130.2487 | 136.3363 | 144.9335 | 157.6865 | 168.1695 | 143.1177 | 121.331 | 146.0346 | 158.2937 | 167.2435 | 167.3675 | 176.5542 | 180.623
Average linear trendline increase in water use
% linear growth pa 3.6%
Trendline growth pa 2.3%

## Slide 29
Historical Use from the Algoa WSS
Chart: AWSS Historical Water Use Breakdown (million m3/a)
| 99/00 | 00/01 | 01/02 | 02/03 | 03/04 | 04/05 | 05/06 | 06/07 | 07/08 | 08/09 | 09/10 | 10/11 | 11/12 | 12/13 | 13/14 | 14/15 | 15/16 | 16/17
NMBM | 72.17 | 73.62 | 74.57 | 77.94 | 80.4 | 79.77 | 83.17 | 87.82 | 94.17 | 98.21 | 91.15 | 85.29 | 89.66 | 95.156 | 104.16 | 107.39 | 110.19 | 107.7531
Small Towns | 1.8939 | 2.3097 | 2.6551 | 2.8756 | 2.9522 | 3.4449 | 4.0216 | 4.4638 | 4.8369 | 6.0787 | 5.5964 | 5.1269 | 5.0637 | 5.1137 | 4.8636 | 6.7064 | 6.7859 | 7.0469
Irrigation | 27.543 | 41.198 | 45.592 | 43.727 | 47.642 | 39.426 | 40.744 | 45.932 | 51.156 | 59.1972 | 43.5919 | 25.6471 | 45.387 | 50.4 | 52.2844 | 47.8404 | 52.9783 | 58.78
Canal Losses | 14.5751 | 19.4202 | 17.7659 | 16.1534 | 14.0661 | 11.3078 | 12.1006 | 10.4177 | 11.2236 | 8.3837 | 6.4794 | 8.967 | 9.624 | 7.624 | 5.9355 | 5.4307 | 6.6 | 7.043
Drought

## Slide 30
2016/17 Use from the Algoa WSS
TOTAL 180.6 million m3/a
Chart: Current potable water use from the AWSS (million m3/a)
| NMBM | Coega IDZ Potable | Small towns | Irrigation | Canal losses & unaccounted-for-water
 | 106.9501 | 0.803 | 7.0469 | 58.78 | 7.043

## Slide 31
2016/17 Use from the Algoa WSS
million m3/a
NMBM | Kouga LM | Hankie & Patensie | GIB | Groendal irrigation | Impofu Dam irrigation | Canal losses | TOTAL USE
107.0 | 5.85 | 1.2 | 54.4 | 2.4 | 2.0 | 7.0 | 180.6
Allocation of 4.5 million m3/a
Plus Coega IDZ potable use of 0.8 million m3/a

## Slide 32
Change:
GIB allocation increased to 60.188 million m3/a
Kouga Dam irrigation water requirements

## Slide 33
Water Balance Conclusions
In 2015/16 water use was in excess of availability
Ph2 of the NLLS becoming operational in July 2017
2016/17 Water requirements reduced slightly as a result of the drought
Water use in 2016/17 exceed water availability, even after implementation of NLLS Ph2
Water use exceeded some allocations, e.g. Kouga LM

## Slide 34
Future Water Requirements

## Slide 35
Water Requirement Scenarios
8 Water Requirement Scenarios developed - combinations of:
  Low growth of 1% compound growth
  Medium growth of 2.5%
  High growth of 3.5% linear growth
  Coega IDP domestic & industrial water projections
  For Kouga LM linear growth of 3.3% high-growth used to be in line with DWS growth estimations, & Thyspunt NPP estimate
  Implementation of the Reserve
  Climate change
Base year for projections is 2016/17

## Slide 36
Coega IDZ Water Requirements

## Slide 37
Kouga LM
Water use exceeds allocation from AWSS
Growth estimates of 3.3% used to be in line with DWS planning
New source needed
Groundwater implementation strongly recommended
Uncertainty regarding development of Thyspunt NPP

## Slide 38
Interventions

## Slide 39
Interventions Considered for Scenario Planning
WC/WDM: 5%, 10% & 15% savings
  Nooitgedagt Low Level Scheme: Phase 3 & Phase 4
Effluent treated to industrial and/or potable standards
  Fish Water Flats WWTW Reuse, phased
  Coega WWTW Reuse, phased
Various groundwater schemes
Lower Sundays River return flows
Seawater Desalination: Swartkops Sea Salt, NMBM (phased) & Thyspunt
Raising of Kouga Dam / Guernakop Dam

## Slide 40
Changes to Interventions
Further allocation of Orange River water to NMBM
  NLLS Phase 4 – assumed potential additional yield of 18.25 million m3/a (50 Ml/d), until this is further clarified
Seawater Desalination
  Marina Sea Salt Desalination included (assumed added yield of 5.5 million m3/a)

## Slide 41
Scenario Planning

## Slide 42
Scenarios Developed
Coega Industrial Water Requirements
Low Growth including Coega Potable: 1% compound growth + Coega potable
High Growth Potable (Reference): 3.5% linear growth + Coega potable
High Growth Potable without WC/WDM: 3.5% linear growth + Coega potable (no efficiency saving from WC/WDM)
Increased supply to Kouga LM: 3.5% linear growth & 3.3% linear growth by Kouga LM + Coega potable, including increased supply to Kouga LM
High Growth including Coega: 3.5% linear growth + Coega potable and industrial
Worst Case: 3.5% linear growth + Coega potable and industrial, with climate change & implementation of the Reserve
Scenario Planning up to 2042

## Slide 43
1. Coega Industrial Water Requirements
Coega WWTW Industrial Reuse Ph 2 Ind
Coega WWTW Industrial Reuse Ph 2 dom
Coega WWTW Industrial Reuse Phase 3 dom
Coega WWTW Industrial Reuse Ph 4 Ind
FWF WWTW Industrial Reuse Ph 2
FWF WWTW Industrial Reuse Ph 1
Coega Industrial water requirements
Coega WWTW Industrial Reuse Ph 3 ind
Coega WWTW Industrial Reuse Ph 1 dom

## Slide 44
2. Low Growth including Coega Potable
Requirement = 1% compound growth + Coega potable
5% WC/WDM
5% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
2 groundwater schemes

## Slide 45
3. High Growth Potable Scenario (Reference)
Requirement = 3.5% linear growth + Coega potable
15% WC/WDM
15% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
Desal – Marina Sea Salt
5 groundwater schemes
Seawater Desal Ph 1

## Slide 46
4. High Growth Potable without WC/WDM
Requirement = 3.5% linear growth + Coega potable
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Kouga dam replacement / raising
Desal – Marina Sea Salt

## Slide 47
5. High Growth Potable with Kouga LM
Requirement = 3.5% linear growth + Koega additional
15% WC/WDM
15% WC/WDM
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 Groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Desal – Marina Sea Salt

## Slide 48
6. High Growth including Coega (pot & ind)
Reuse Coega - FWF WWTW
15% WC/WDM
15% WC/WDM
Requirement = 3.5% linear growth + Coega pot & ind
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
Reuse Coega – Coega WWTW
Desal – Marina Sea Salt
5 Groundwater schemes
Reuse Coega – Coega WWTW

## Slide 49
7. Worst Case Scenario
Reuse Coega – ex FWF WWTW
15% WC/WDM
15% WC/WDM
Requirement = 3.5% linear growth + Coega pot & ind
Reuse Coega – ex Coega WWTW
Nooitgedagt Low Level Scheme Phase 3
Groundwater Coega Fault
Lower Sundays Return Flows
NLLS Phase 4
5 groundwater schemes
Seawater Desal Ph 1
Seawater Desal Ph 2
Seawater Desal Ph 3
Desal – Marina Sea Salt
Kouga dam replacement / raising
Reuse Coega – ex Coega WWTW

## Slide 50
Scenario Conclusions
Current shortages caused by drought
Effective WC/WDM essential for NMBM & Kouga LM
Complete NLLS Ph3 & remove bottlenecks in delivery
Planning of interventions should proceed due to long implementation lead times & uncertainty in terms of growth in water requirements
  May be difficult to timeously implement next interventions after NLLS Ph 3 and Coega Kop groundwater schemes
Groundwater schemes to be pursued by NMBM & Kouga LM (forms part of drought actions)
Thyspunt NPP will have limited impact from water perspective (assuming desalination) but needs supply during construction

## Slide 51: - Thank you -

## Slide 52
7 Water Requirement Scenarios
Coega Industrial Water Requirements
Low Growth including Coega: 1% compound growth + Coega potable and industrial
High Growth Potable: 3.5% linear growth + Coega potable (Reference scenario)
High-Growth Potable without WC/WDM: 3.5% linear growth, with no efficiency savings
Increased supply to Kouga LM: 3.5% linear growth plus Kouga LM growth plus Thyspunt NPP
Base Year = 2016/2017

## Slide 53
7 Water Requirement Scenarios
High Growth including Coega: 3.5% linear growth + Coega potable and industrial
Worst Case: Same as Reserve Scenario, plus climate change
Base Year = 2016/2017