## Slide 1: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 18 September 2019

## Slide 2: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 2: Attendance and Apologies

## Slide 3: Agenda

## Slide 4: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 4: Purpose of the Meeting

## Slide 5: Background to this Assignment
Reconciliation Strategy for the Mbombela Municipal area was developed (2014)
Recommends sequence of management and infrastructural interventions required to maintain acceptable assurances of supply to the users.

## Slide 6: Outcomes of previous assignment
Options for reconciling increasing water requirements with the current supply in the Crocodile and Sabie Catchments included:
Water Conservation and Demand Management (WC/WDM)
Removal of Invasive Alien Plants (IAPs)
Reallocation of water (pending DWS approval)
System Operating Rules for Primkop Dam and other upstream dams (yield optimisation)
Groundwater development
Rain and fog harvesting

## Slide 7: Outcomes of previous assignment
Regional Dam: 3 possible schemes were identified in the Crocodile River catchment:
  Montrose Dam (eliminated – other options more economical)
  Mountain View Dam (to be investigated further – feasibility study)
  Strathmore off-channel storage dam (to be investigated further – feasibility study)
Please visit: http://www6.dwa.gov.za/iwrp/projects.aspx for all project related information

## Slide 8: Why Continuation of a Strategy? (This Study)
  Water balances need to be continuously monitored / investigated and the strategy regularly updated to remain technically relevant.
  Ensures that intervention planning can be implemented taking into account any changes that may impact on the projected water balance.
  Study Objective: In-depth review, systematically update and improve the water resource reconciliation strategy so that it remains relevant, technically sound, economically viable, socially acceptable and sustainable and thus enabling the implementation of the strategy by the relevant authorities.

## Slide 9: Purpose of the Meeting
  Overview of study activities since StraSC Meeting 2
  Feedback on Strategy interventions

## Slide 10: Matters Arising: Action list

## Slide 13: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 7: Status of Strategy (2014) Interventions

## Slide 14
Intervention (from 2014 Strategy) | Representative Feedback
Addressing Unlawful Irrigation Use (Compliance Monitoring and Enforcement) | IUCMA: A Mbalathi
WC/WDM Urban | City of Mbombela: T Botha Bushbuckridge LM: R Baloyi
WC/WDM in the Irrigation Sector and Relinquishing of Water Savings | Dept Agric: Marius van Rooyen
Water Re-allocation | IUCMA: T Sawunyama
License conversions | DWS HO: Either P Mlilo or K Mandaza
Removal of IAPs | Working for Water: B Mashabane
Groundwater Development | IUCMA: T Sawunyama
Operationalisation of the Reserve | KNP: E Riddell
Pre-Feasibility Study into Dams & thereafter New Dam Constructed | DWS HO: K Bester
System Operating Rules for Sabie River | PSP: C Seago
Operating Rules for Primkop Dam | PSP: C Seago

## Slide 15
Progress on Implementation of the EWR in Crocodile and Sabie Rivers
Continuation of the Mbombela Reconciliation Strategy, Sept 2019

## Slide 16
Status-Quo: Ecological Reserve Environmental Water Requirements

## Slide 17
Implementation of Strategic Adaptive Management for freshwater protection under the South African national water policy (McGloughlin et al, 2011, Water Research Commission)
Adaptive Management Operationalization for Rivers

## Slide 18: Functional governance systems: Feedback loops Establishment of the CROCOC c. 2009
ICMA
Monitors benchmark
(‘Reserve)
KNP
CMIB
Users
Kwena Dam bailiff
DWA RO
NDWA
Mozambique
Monitor benchmark
(International obligation)
Monitors various benchmarks
Adapted from Pollard and du Toit. 2011.

## Slide 19
KNP Rivers: Management Actions
Instituted work by McLoughlin et al. 2011.
‘History, rationale, and lessons learned: Thresholds of potential concern in Kruger National Park river adaptive management’,
Koedoe 53(2)

## Slide 20
Edward Riddell, Sharon Pollard, Stephen Mallory & Tendai Sawunyama (2014)
Hydrological Sciences Journal
Brian Jackson (2015)

## Slide 21
Drought Responses?

## Slide 22
Social Media: Real-Time Communication, Accountability

## Slide 23
Flows Kruger Western Boundary – Crocodile River @ Tenbosch

## Slide 24
Flows Kruger Western Boundary – Sabie @ Kruger Gate

## Slide 26
Thank you!

## Slide 27
Intervention (from 2014 Strategy) | Representative Feedback
Addressing Unlawful Irrigation Use (Compliance Monitoring and Enforcement) | IUCMA: A Mbalathi
WC/WDM Urban | City of Mbombela: T Botha Bushbuckridge LM: R Baloyi
WC/WDM in the Irrigation Sector and Relinquishing of Water Savings | Dept Agric: Marius van Rooyen
Water Re-allocation | IUCMA: T Sawunyama
License conversions | DWS HO: Either P Mlilo or K Mandaza
Removal of IAPs | Working for Water: B Mashabane
Groundwater Development | IUCMA: T Sawunyama
Operationalisation of the Reserve | KNP: E Riddell
Pre-Feasibility Study into Dams & thereafter New Dam Constructed | DWS HO: K Bester
System Operating Rules for Sabie River | PSP: C Seago
Operating Rules for Primkop Dam | PSP: C Seago

## Slide 28: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 8: Overview of Study Activities

## Slide 29
STUDY PROGRAMME

## Slide 30: STUDY TASKS
TASK NUMBER | TASK DESCRIPTIONS
1 | Inception and Literature Review
2 | Economic Growth and Demographic Analysis
3 | Water Requirements and Return Flows
4 | Water Conservation and Demand Management
5 | Monitoring Network Expansion and Data Capturing
6 | Water Resources Analysis
7 | Infrastructure and Cost Assessment
8 | Preliminary and Updated Reconciliation Strategy
9 | Ad Hoc Support
10 | Capacity Building and Training
11 | Stakeholder Engagement
12 | Study Reports
13 | Study Management

## Slide 34: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 9: Current Progress

## Slide 35: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 9.1: Water Resources Assessment

## Slide 36: 9.1: TASK 7: Water Resources
  Hydrology, system yields, water resource model configuration
  Previous Water Resources Studies:
    DWS: Inkomati Water Availability Assessment (2009)
    DWS: IWAAS Maintenance (2012)
    DWS: Classification Study (2013)
    DWS: Reconciliation Strategy Study (2014)
    IUCMA: Operational Support (ongoing)
    IUCMA: Hydrology updates: Croc East (draft completed)
  Water Resources Summary, Mbombela Recon Strategy (2014)
  Water reconciliation strategy update for the schemes in the Sabie and Sand river system Bushbuckridge Local Municipality (2016)

## Slide 37: Mbombela Recon (2014) Water Resources Report Yields from IWAAS

## Slide 38: Recon (2014) Water Balance
Resource including EWR: 14.6 million m3/a

## Slide 39
Bushbuckridge Recon (2016)

## Slide 40
Inyaka WTW: 36.5 million m3/annum
Sabie River: 14 million m3/annum
Groundwater: 10.5 million m3/annum
Bushbuckridge Recon (2016)

## Slide 41: Hydrology
  IWAAS
    Major study, detailed landuse evaluation, external review
    WRYM configured, yields produced
  IWAAS Maintenance
    Small adjustments to hydrology in some catchments due to evaporation error
  Current IUCMA update: Crocodile East
  TSG 6 decision: Incorporate new hydrology in future Strategy Update once approved, remain with IWAAS Maintenance for this Strategy update and focus on model configuration enhancements

## Slide 42: Comparison / Review (Natural MAR million m3/a)
 | 1920-2004 | 1920-2016
Tertiary | IWAAS Maint. | Update (2019)
X21 | 467.3 | 493.8
X22 | 381.9 | 394.7
X23 | 195.4 | 210.5
X24 | 106.6 | 112.0
Total | 1151.1 | 1211.0
Summary: Update results in higher MAR than original IWAAS, despite evidence of drought/low rainfall in recent years. Remaining with IWAAS hydrology is a conservative approach

## Slide 43
140 Sub-catchments

## Slide 44: Model Updates / Enhancements
  IWAAS WRYM used as base
    2 individual model configurations (1 Sabie/Sand, 1 Crocodile East)
  Landuse remains as per IWAAS (Agreed in Water Requirements Task of Study)
  Combination into 1 WRPM configuration to assess future growth in water requirements and integrated WRM
  Incorporation of Demand Centres
  Incorporation of Irrigation
  Incorporation of EWRs
  Configuration of operating rules

## Slide 45: Demand Centres

## Slide 46
Acornhoek

## Slide 47: Irrigation
  Irrigation schemes & diffuse irrigators
  Based on IWAAS information
  Summary (6 schemes simulated at 22 abstraction points):
Board | Demand (million m3/a)
Croc board | 312.9
Elands IB | 7.9
Kaap | 36.4
Sabie Board | 10.9
White river | 30.4
White Waters IB | 15.6
Total | 414.1

## Slide 48: EWRs
  7 sites on Crocodile, 8 sites on Sabie/Sand
  Classification undertaken, 2014
    WRYM not used for Classification, therefore EWR structures and locations not included
    No specific report relating to water resources analyses available from Classification
    Two Gazettes have been published
      January 2016: Proposed Classes of Water Resources and Resource Quality Objectives for the Catchments of the Inkomati
      November 2017: Proposed Reserve Determination of Water Resources for the Inkomati River Catchment
    Incorporated EWR structures into model

## Slide 50
“All three the proposed scenarios (Sc C3, C62 and C82) are where the “PES” releases are the target EWR and allow progressive improvements in both the ecological health as well as the socioeconomic conditions in future.”

## Slide 51: Operating Rules (supplied by IUCMA)
Catch-ment | Dam trigger | Dam level % | Restriction % | Supply factor | Sector
Croc | Kwena | 70 | 35 | 0.65 | Irrig
 |  | 55 | 60 | 0.4 | 
 |  | 10 | 100 | 0 | 
 |  | 60 | 10 | 0.9 | Dom
 |  | 40 | 20 | 0.8 | 
 |  | 20 | 30 | 0.7 | 
 |  | 10 | 10 | 0.9 | Ind
Sabie | Inyaka | 65 | 40 | 0.6 | Irrig
 |  | 20 | 60 | 0.4 | 
 |  | 60 | 10 | 0.9 | Dom
 |  | 40 | 20 | 0.8 | 
 |  | 20 | 30 | 0.7 | 

## Slide 52: Scenarios & Results: Sabie-Sand
  With and without restriction rule
  Groundwater contribution (10.5 million m3/a)
  Bushbuckridge Transfer Pipeline (25 million m3/a capacity)
  Inyaka Starting storage (May 2018): 78%
  Inyaka Dam yield (IWAAS) including EWR:

## Slide 53
Probability distribution (boxplot)
Results for generated sequences
0 % 5.0 % 25 % 50 % 75 % 95 % 100 %
Percentage of sequence results exceeding given value

## Slide 54
98% assurance of supply
=
2% risk of non-supply
=
1 in 50 year recurrence interval
Typical Urban criteria

## Slide 55
No restriction rule in place
2% Risk of non-supply
98% Exceedance probability of storage
Bushbuckridge Supply
Inyaka Dam
Hoxani Supply
Marite Supply
50
150
20
5
2018
2040

## Slide 56
Including BTP Capacity
Excluding BTP Capacity
2025
2037
Bushbuckridge Supply
Inyaka Dam
Bushbuckridge Supply
Inyaka Dam

## Slide 57
Including restriction rule
Dam 60% = 10% restrict
Dam 40% = 20% restrict
Dam 20% = 30% restrict
Unused Storage
Bushbuckridge Supply
Inyaka Dam
Hoxani Supply
Marite Supply
50
150
20
5
2018
2040

## Slide 58
2002
2019

## Slide 59: Sabie-Sand: Summary
  Bushbuckridge Transfer Pipeline capacity restricts users from year 2025
  Resource sufficient to meet growing requirements and EWR up till 2037 (excluding restrictions)
  Restriction Rule needs to be addressed as it is currently too strict and does not provide sufficient utilisation of resource
  Recommend adaptive drought operating rules which dynamically change the reservoir level restriction trigger as water requirements increase over time

## Slide 60: Scenarios & Results: Crocodile East
  With and without restriction rule
  Kwena Dam Starting storage (May 2018): 75%
  Kwena Dam yield (IWAAS) including EWR:

## Slide 61
No restriction rule in place
Dam fails at 75% probability
2% risk of non supply
Supplied better, own resources
Crocodile Irrigation Supply
Kwena Dam
Mbombela (Nelspruit WTW) Supply
White River Supply
300
180
30
12
2018
2040

## Slide 62
Including restriction rule
Rule protects dam
2% risk of non supply
Dam 70% = 35% restrict
Dam 55% = 60% restrict
Dam 10% = 100% restrict
Crocodile Irrigation Supply
Kwena Dam
Mbombela (Nelspruit WTW) Supply
White River Supply
300
180
2018
2040
12
30

## Slide 63: Other Studies for Comparison
  Inkomati Water Management Area: Internal Strategic Perspective (ISP, 2004):
    Yield at 98% assurance of supply (1 in 50 year)
    Crocodile system: 264 million m3
    Requirements (2003 development level): 413 million m3
    Deficit: 149 million m3
  Progressive Realisation of the IncoMaputo Agreement (PRIMA, 2011)
    Yield at 90% assurance of supply (1 in 10 year)
    Crocodile system: 446 million m3
    Requirements: 557 million m3
    Deficit: 111 million m3

## Slide 64: Summary and Way forward
  Base results indicate the Crocodile system is in severe deficit
  Determine system yield availability and compare with previous studies
  Test/recommend operating rules
  Include interventions & reassess risk of supply failure and quantify restrictions
  Produce annual water balance plots

## Slide 65: CONTINUATION OF WATER REQUIREMENTS AND AVAILABILITY RECONCILIATION STRATEGY FOR THE MBOMBELA MUNICIPAL AREA (Crocodile Sabie River System Reconciliation Strategy) Strategy Steering Committee Meeting StraSC 3 Item 9.2: Infrastructure and Cost Assessment

## Slide 66: Agenda Item 9.2: task 7: INFRASTRUCTURE AND COST ASSESSMENT Evaluation of the infrastructure intervention options that were identified during the previous reconciliation strategy and the related cost and financial implications.

## Slide 67: Infrastructure: Groundwater Sabie catchment: - Groundwater availability generally low. Groundwater can however be found where dykes and shear zones occur. - Further studies will be required to develop groundwater. Crocodile catchment: - Boreholes are usually drilled as the need arises on request of a local community. - Groundwater availability generally low. Groundwater can however be found where dykes and shear zones occur. Feedback with respect to groundwater was provided earlier on in the agenda.

## Slide 68
Infrastructure: Dams (Sabie and Sand River catchment):
Two dams were identified that can augment the water resources in the catchment:
Dingleydale Dam.
Located at the confluence of the Nwarhele and Mtlumuvi river
New Forest Dam
Located at the confluence of the Klein Sand and Sand rivers
These dam sites can be considered should the need arise for an augmentation of the water resources in the catchment.

## Slide 69
Infrastructure: Dams (Crocodile River catchment):
A total 5 dams were identified that can augment the water resources in the catchment:
Raising the Primkop dam (White River).
Boschjeskop Dam (Nels River).
Montrose Dam (Crocodile River).
Mountain View Dam (Kaap River).
Strathmore Dam (Off-channel).

## Slide 70
Sabie River Catchment
Dingleydale Dam
Crocodile River
Catchment
New Forest Dam
Strathmore Dam
Mountain View Dam
Montrose Dam
Boschjeskop Dam
Location of proposed dams

## Slide 71
Infrastructure: Proposed Dams (Crocodile River catchment):
Raising the Primkop Dam
Capacity = 15 Mm3
Yield = 10 Mm3/a
Height = 31.4 m
Low water cost (URV)
Boschjeskop Dam
Capacity = 100 Mm3
Yield = 19.5 Mm3/a
Height = 45 m
Higher water cost (URV)
Montrose Dam
Capacity = 12.2 Mm3
Yield = 60 Mm3/a
Height = 30 m
High water cost (URV), High environmental impact

## Slide 72
Infrastructure: Proposed Dams (Crocodile River catchment):
Mountain View Dam
Capacity = 229 Mm3
Yield = 34 Mm3/a
Height = 90 m
Low water cost (URV), low environmental impact
Strathmore Dam
Capacity = 59 Mm3
Yield = 76 Mm3/a
Height = 32 m
Low water cost (URV), located next to a Magnesium mine

## Slide 73
Infrastructure: Matsulu Abstraction
At times of low flows in the Crocodile River, the Matsulu Abstraction Works runs short of water due to the diversion of flow into the Van Graan Canal upstream of the abstraction works.
A permanent solution for the problem needs to be identified.

## Slide 74
Infrastructure: Matsulu Abstraction
The following possible solutions had been identified:
Revising the permit for the Van Graan canal to make allowance for the domestic water requirements of Matsulu. Current permit allows for 7.8 m3/s to be diverted into the canal.
Moving the Matsulu abstraction pumps to a point downstream of the canal discharge point.
Moving the Matsulu abstraction pumps to a point upstream of the canal entry point (The Kaapmuiden Weir)

## Slide 75
Questions?

## Slide 76: IMPLEMENTATION AND MAINTENANCE OF THE WATER RECONCILIATION STRATEGY FOR RICHARDS BAY AND SURROUNDING TOWNS Technical Support Group Meeting (TSG) 6 Item 10: Discussion and Comments