## Slide 1
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Water Requirements Workshop
Presented by:
Erik van der Berg
Aurecon
20 May 2013

## Slide 2
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Agenda
Background
Historical & planned future water use
Usage vs Allocations
Drivers of water use
Scenarios

## Slide 3
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Background

## Slide 4
Sub-Title here (if needed)
PRESENTATION TITLE HERE (if needed)
Purpose of DWA: NWRP
DWA D: NWRP is responsible for strategic level planning to ensure sufficient and sustainable water resources for the country
The planning approach is to seek reconciliation of the available water resource/s with growing requirements

## Slide 5
Sub-Title here (if needed)
PRESENTATION TITLE HERE (if needed)
DWA Planning on two fronts
Planning is highly structured and is guided by:
  National Water Act
  National Spatial Development Perspective (NSDP)
  National Water Resource Strategy (national)
  Integrated Strategic Perspectives (catchments)
  Reconciliation strategies (metros)
  All towns strategy studies
Ad hoc
  Where problems require urgent action

## Slide 6: NSDP: Key demand centres

## Slide 7: Reconciliation Strategies for large systems and metros
Completed
  Western Cape
  Amatole system
  Vaal River
  Crocodile West
  KZN Coastal Metropolitan areas
  Algoa
  Bloemfontein
  Outeniqua
Current
  Olifants system
  Mbombela system
  Levuvhu-Letaba
  Richards Bay

## Slide 8
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Purpose of Study
Development of a strategy for interventions to meet possible water requirements in Richards Bay & surrounding towns up to 2040
Determine potential options / groups of options – that form reconciliation scenarios – each of which could potentially be implemented
Identify information needed & time frame to implement the strategy

## Slide 9
Purpose of Workshop
Opportunity for key stakeholders to comment on water use and future water requirements
Review & agree on historic/current water requirements in the supply area
Review & comment on proposed future water requirements scenarios to accommodate potential growth
Agree on scenarios to develop for further planning
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 10
Strategy Area
Primarily the uMhlathuze Local Municipality
Extended to include RBM mining areas, Fairbreeze mine & some rural domestic supply areas
Considered factors that may expand the strategy area
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 11
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 12
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Historical & planned future water use

## Slide 13
Water Supply Sectors
Industrial (bulk)
Domestic (potable supply/light industrial)
Irrigation
Forestry
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 14
Historical Water Use
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Chart: Historical Water Use
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Industrial | 70.5715 | 72.4665 | 69.2202 | 68.8611 | 56.8099 | 54.4913
Domestic | 34.8827 | 34.0135 | 32.3703 | 36.6241 | 38.9545 | 42.5797
Total | 105.4541 | 106.48 | 101.5905 | 105.4851 | 95.7644 | 97.0711

## Slide 15
Water Efficiency
City of uMhlathuze
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Up to 31 % Non-Revenue Water (NRW) in Richards Bay (5.3 Mm3/a)
Some initiatives in place (leak detection, pressure reduction)
The 5-Year Strategic Management Plan identifies 19% NRW target as practical limit of what is achievable
Metering & monitoring is critical to ensure optimum revenue collection
Further opportunities - active leakage control, water efficient fittings in new developments (through by-laws), continued raising of awareness
Successful implementation of WC/WDM requires adequate budgeting, resourcing and commitment by users and authorities

## Slide 16
Water Efficiency (cntd)
Mhlathuze Water
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
The Water Resources Management Unit raises awareness and undertakes education campaigns on water conservation
Participates in the Working for Water Program in which over 6000 hectares cleared during the 2012/13 financial year

## Slide 17
Water Efficiency (cntd)
Bulk industries
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
There is awareness of necessity for water conservation strategies
Plans include:
  Internal recycling of water in processes
  Stormwater capture and re-use
  Increased efficiency

## Slide 18
Information Discrepancies
Discrepancies in historical water use values
  Mondi/ Mhlathuze Water figures differ
  Foskor (clarified)/ Mhlathuze Water figures differ
  RBM and Tronox/ Mhlathuze Water
Discrepancies in legal water-use figures
  Mondi RB allocation (DWA: 110Ml/day, MW: 100Ml/day, Mondi: 90Ml/day)
Incomplete historical usage statistics
  Hillside & Bayside
  Mondi Felixton
  RBCT
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 19
Water Treatment Works
Mzingazi WTW
Nsezi WTW
Esikhaleni WTW
Ngwelezane WTW
Chart: Annual Water Production
| Esikhaleni | Ngwelezane | Mzingazi | Nsezi
Annual Water Production (Mm3) | 10.4983 | 2.0742 | 21.7694 | 38.1254
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 20
Major Industries
Mondi R’Bay
RBM
Tronox (Hillendale/Fairbreeze)
Foskor
Hillside & Bayside Aluminium (BHP Billiton)
Tongaat Hulett
Mondi Felixton
R’Bay Coal Terminal
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 21
Major Industries
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Chart: Current Industrial Usage and Allocations
| Mondi Richards Bay | RBM - total | Foskor - total | Tronox - Hillendale | Mondi Felixton | Hillside | Tongaat Hulett | RBCT | Bayside - raw
Allocations | 32.85 | 30 | 10.439 | 11.4829 | 3.15 | 0 | 1.888 | 0 | 0.34218
Current Usage | 23.6147 | 15.3377 | 7.3145 | 3.751 | 2.2156 | 0.78 | 0.71 | 0.43361 | 0.34218
Mm3/a | Mondi Richards Bay | RBM - total | Foskor - total | Tronox - Hillendale | Mondi Felixton | Hillside | Tongaat Hulett | RBCT | Bayside - raw
Current Usage | 23.61 | 15.34 | 7.31 | 3.75 | 2.22 | 0.78 | 0.71 | 0.43 | 0.34
Allocation | 32.85 | 30.00 | 10.44 | 4.19 | 3.15 | - | 1.89 | - | 0.34

## Slide 22
Mondi Richards Bay
Allocation 90Ml/day (32.85Mm3/a)
Historical use 60-70Ml/day
Potable water supplied (Nsezi WTW)
Own WWTW (55Ml/day)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss: Clarification of usage statistics

## Slide 23
Richards Bay Minerals (RBM)
Total allocation 82Ml/day (30Mm3/a)
Historical use 40-70Ml/day
Three sources for raw water abstraction:
    Mfolozi River, Lake Nhlabane, Lake Nsezi
Mines and smelters
Zulti South expansion (2017)
Own WTW and WWTW
Stormwater/process water reused
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
© Thys van der Merwe
Discuss: Clarification of allocations

## Slide 24
Foskor – Acid Division
Total allocation 29Ml/day (10Mm3/a)
Historical use 15-30Ml/day
Two grades supplied: clarified and potable
Nsezi WTW and Mzingazi WTW
Effluent disposal by Alkantstrand Pump Station (pipelines B and C)
Use some recycled water from Hillside
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss: Clarification of usage statistics

## Slide 25
Tronox (formerly Exxaro)
Current allocation (Hillendale Mine) 31.5Ml/day (11.48Mm3/a)
Fairbreeze Mine planned usage 48.0Ml/day (2017-2027)
Port Durnford Mine planned usage 55.5Ml/day (2027-2058)
Raw water abstraction from Mhlathuze Weir
Central processing plant in Empangeni
Supply from Empangeni urban supply (Nsezi WTW)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss: Clarification of usage statistics

## Slide 26
BHP Billiton (Hillside & Bayside)
Planned phasing out of Bayside Aluminium
Hillside usage 2.14Ml/day (0.78Mm3/a)
Treated water supplied from Mzingazi WTW
Effluent disposal by Alkantstrand Pump Station (pipeline A)
Provides Foskor with some recycled water
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss: Clarification of usage statistics
Hillside
Bayside

## Slide 27
Richards Bay Coal Terminal (RBCT)
Previously large user
Water use efficiency project has lead to diminished usage in recent years
Less than 1Mm3/a use
Potential future expansion
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 28
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Mondi Felixton
Raw water abstraction from Mhlathuze River
Use Tongaat Hulett WTW and WWTW
Usage 6.07Ml/day
Tongaat Hulett
Raw water abstraction from Mhlathuze River
Own WTW and WWTW
Usage 1.95Ml/day

## Slide 29
Industrial Development Zone (IDZ)
Future identified developments in several phases
Phase 1 in Richards Bay city area
  Phases 1A, D & F
Phase 2 to the north (outside municipal area)
Earlier phases supplied by Mzingazi WTW
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 30
Sub-Title here (if needed)
PRESENTATION TITLE HERE (if needed)
Urban Domestic Use
Larger centres: Richards Bay, Empangeni
Smaller centres: Ngwelezane, Nseleni, Esikhaleni, Felixton, Vulindlela
Rural and tribal areas
Current Usage |  | 
Urban Centre | Annual (Mm3) | Daily (Ml)
Empangeni | 9.34 | 25.58
Richards Bay | 14.18 | 38.85
Esikhaleni | 11.16 | 30.56
Nseleni | 4.28 | 11.71
Ngwelezane | 2.54 | 6.95
Total | 41.48 | 113.66
Chart: 
| Empangeni | Richards Bay | Esikhaleni | Nseleni | Ngwelezane
Domestic Usage | 9.3369 | 14.1811 | 11.155 | 4.276 | 2.5352

## Slide 31
Irrigation
Primarily supplied from Goedertrouw Dam / Mhlathuze River
Constitutes a Government Water Control Area
Allowance made for (further) development of small irrigators
Otherwise water requirement expected to remain constant over study period
Verification and Validation process commenced 2006
  66% of quota allocated
Compulsory licensing exercise
  Final volume expected to be in the order of 120Mm3/a
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 32
Other water uses
Forestry
  Extensive commercial forestry
  Owned mostly by Mondi and Sappi
  Constitutes a stream-flow reduction activity, not a direct user
  Interest for further expansion, but DWA unlikely to grant further licences
  Some community projects may possibly be licensed
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 33
Summary of current use
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Ceri, please make 2 pie charts as follows:
uMhlatuze WSS – industrial & domestic use
Mhlatuze catchment water balance; i.e. increased domestic use + irrigation + forestry ???
Chart: 
| Industry | Domestic
Mhlathuze WSS | 55.2064 | 41.4843

## Slide 34
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Usage vs Allocation

## Slide 35
Compulsory licensing
Commenced 2010, nearing completion
Aimed to free up allocated, but un-utilised, water
  Clarification on possible reallocation of industrial water use allocations
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 36
Current Usage
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Sector | Usage (Mm3/a)
Industrial | 55.21
Domestic | 41.48
Irrigation | 120.00
Chart: Current Usage
| Industrial | Domestic | Irrigation
Mhlathuze WSS | 55.2064 | 41.4843 | 120
Measurable sectors: industrial, domestic, irrigation
SFRA (indirect users): forestry, dryland agriculture, alien vegetation

## Slide 37
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
 |  | Current Usage |  | Allocation | 
Supply Sector | User | Annual (M3/a) | Daily (Ml/day) | Annual (M3/a) | Daily (Ml/day)
Industry | Mondi Richards Bay | 23.61 | 64.70 | 32.85 | 90.00
 | RBM | 15.34 | 42.02 | 30.00 | 82.19
 | Tronox - Hillendale | 3.75 | 10.28 | 11.48 | 31.46
 | Foskor | 7.31 | 20.04 | 10.44 | 28.60
 | Mondi Felixton | 2.22 | 6.07 | 3.15 | 8.63
 | Tongaat Hulett | 0.71 | 1.95 | 1.89 | 5.17
 | Bayside | 0.52 | 1.44 | 0.34 | 0.94
 | Hillside | 0.78 | 2.14 | - | -
 | RBCT | 0.43 | 1.19 | - | -
 | Tronox - Fairbreeze | - | - | 22.69 | 62.2
 | TOTAL | 55.21 | 151.25 | 90.49 | 247.93
Domestic | Empangeni | 9.34 | 25.58 | 13.51 | 37.00
 | Richards Bay | 14.18 | 38.85 | 9.13 | 25.00
 | Esikhaleni | 11.16 | 30.56 | 5.48 | 15.00
 | Nseleni | 4.28 | 11.71 | 0.00 | 0.00
 | Ngwelezane | 2.54 | 6.95 | 2.92 | 8.00
 | TOTAL | 41.48 | 113.66 | 31.03 | 85.00
 | GRAND TOTAL | 96.69 | 264.91 | 121.52 | 332.93

## Slide 38
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Drivers of water use

## Slide 39
Drivers of Water Use
Rainfall
Population growth
Economic growth
UAW
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 40
Rainfall variability
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Chart: Annual Rainfall 1970-2000
| 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000
 | 1739.4 | 1434.12 | 1290 | 1008.12 | 1304.88 | 1637.88 | 1650.36 | 1296.6 | 1015.08 | 891.6 | 1265.76 | 911.4 | 800.28 | 2167.2 | 1267.56 | 1025.88 | 2136.6 | 1216.68 | 1285.2 | 1298.16 | 1464.12 | 597.6 | 785.64 | 991.44 | 1248.72 | 1404.84 | 1096.2 | 884.4 | 1172.04 | 929.64 | 926.16

## Slide 41
Population growth
Population growth
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Urban centres include Richards Bay, Empangeni, former KZN government townships, Felixton (home to Tongaat-Hulett and Mondi), 5 Traditional Authority areas, 21 rural settlements and 61 farms.
The current population is estimated at 378 000
The estimated population growth rate is a moderate 1, 5% p.a, influenced negatively by HIV/Aids and positively by inwards migration.

## Slide 42
Economic Growth
Socio-Economic considerations
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Socio-economic standards in the WMA are below national average.
Over 40% of the population subject to poverty.
Municipal projects and job creation aim to alleviate poverty levels.
Unemployment ~ 19% (urban areas) and ~ 50% in rural areas.
Rapid industrial growth has not translated proportionally to job numbers.
Limited development of downstream business opportunities contributes to above phenomenon.

## Slide 43
Economic Growth
Economic growth
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
The harbour and transport infrastructure are enablers of an economy relatively more competitive than rest of RSA (ito manufacturing, transport and agriculture.
The small local consumer base and limited downstream business activities suggest that medium term growth will remain driven by large export-orientated industrial developments.
The success of the IDZ is subject to market influences, electricity price and stability of supply, and stable economic environment for investors.

## Slide 44
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Scenarios

## Slide 45
Future Water Requirements by Sector
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Supply Sector | Users
Current industries (fixed) | Mondi R’Bay, Mondi Felixton RBM, Foskor, Hillside Aluminium, Bayside Aluminium potable , Tongaat Hulett
Current industries (variable) | Tronox Hillendale & Fairbreeze, Bayside Aluminium, RBCT/harbour
New industries (IDZ) | IDZ identified new industries (Phases 1 and 2)
New industries (other) | Further new industries/mines (Jindal mine etc.)
Urban (domestic & light industrial) | Increased supply from WTWs in City of uMhlatuze
 | Increased supply to other areas in or from Mhlatuze catchment
 | Significant expansion outside municipal boundary: Mtubatuba / Mpukunyoni Scheme from Nseleni WTW
Irrigation | Existing irrigation after compulsory licensing
 | New irrigation (no growth allowed for)
SFRAs (plantation forestry) | Existing SFRAs (no growth allowed for)
Discuss Table 3.3 on page 19 of Workshop BID

## Slide 46
Industrial – fixed requirements (Mm3/a)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss Table 3.3 on page 19 of Workshop BID
Supply Sector | User | Alloca-tion | Use 2013 | Notes on future water requirements
Industries Fixed require-ments | Mondi R’Bay | 32.85 | 25.55 | Allow allocation over full period
 | Mondi Felixton | 3.15 | 2.22 | Allow allocation over full period
 | RBM – total (Mfolozi, Nhlabane, Nsezi) | 30.00 | 24.71 | Allow 30 Mm3/a for full period. Assume 30% supply from Mfolozi River
 | Foskor - clarified | 5.48 | 4.67 | Allow allocation over full period
 | Foskor - potable | 4.96 | 3.41 | Allow allocation over full period
 | Hillside Aluminium | - | 0.78 | Current use continues over full period
 | Bayside Alumi-nium potable | - | 0.18 | Allow 30% of current use over full period
 | Tongaat Hulett, Felixton | 1.89 | 0.79 | Full allocation over period: potential increased use of 1 million m3

## Slide 47
Industrial – Variable Requirements (Mm3/a)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss Table 3.3 on page 19 of Workshop BID
Supply Sector | User | Alloca-tion | Use 2013 | Notes on future water requirements
Industries variable | Tronox - Hillendale | 11.48 | 3.77 | Mine closing with rehabilitation being done – phase out over 3 yrs.
requirements | Tronox - Fairbreeze | 22.69 | - | 48.8 Ml/d from 2017 to 2027 for Fairbreeze. 55Ml/d thereafter for Port Durnford mine
 | Bayside Aluminium raw | - | 0.34 | Raw water: phase out over 3 yrs, starting with 30% of current use.
 | RBCT and harbour | - | 0.26 | Current use continues until 2020 when it increases by 20%

## Slide 48
New Industrial Requirements (Mm3/a)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss Table 3.3 on page 19 of Workshop BID
Supply Sector | User | Notes on future water requirements
New industrial users | IDZ planning | According to IDZ Phases 1 & 2 (incl. Pulp United as part of Phase 1D) Scenarios of 25%, 50%, 75% and 100% of IDZ planning
 | Further new (Jindal mine etc.) | Scenarios of 0%, 1%, 2% additional growth

## Slide 49
Urban/potable Requirements (Mm3/a)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss Table 3.3 on page 19 of Workshop BID
Supply Sector | User | Alloca-tion | Use 2013 | Notes on future water requirements
Urban (domestic / light industrial) | Supply from WTWs in uMhlatuze LM | 31.0+ municipal | 41.5 | Scenarios of 1%, 2%, 3.5% growth
 | Increased supply to other areas located in or supplied from Mhlatuze catchment | 5.0 | 5.5 | Scenarios of 1%, 2%, 3% and 4% growth
 | Significant expansion outside municipal boundary | - | - | Planning for Mtubatuba / Mpukunyoni Scheme from Nseleni WTW

## Slide 50
Irrigation & Forestry Requirements (Mm3/a)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Discuss Table 3.3 on page 19 of Workshop BID
Supply Sector | User | Alloca-tion | Use 2013 | Notes on future water requirements
Irrigation | Existing irrigation after compulsory licensing | 120 |  | Revised allocations over full period
 | New irrigation | - | - | Increased use not included
SFRAs (forestry) | Existing SFRAs | - | - | Possibility for doubling of forestry over period – not included Possibility of increased dryland sugar cane – not included

## Slide 51: Population growth scenarios
Population number
Years
350 000
0.5 % pa
3.5 % pa
2014
2040
High
Low

## Slide 52: Economic growth scenarios
GGP (Rands million)
1 % pa
6 % pa ?
Years
2014
2040
Low
High

## Slide 53: Per capita income
GGP per capita
Years
High economic growth rate
Low population growth rate
Low economic growth rate
High population growth rate

## Slide 54: Translating population and economic growth into water demand
Water use
Years
2040
1970
2014
High eco
High pop
High eco
Low pop
Low eco
Low pop

## Slide 55: Forecasts in context
Key Factors affecting forecast:
Starting point
Uptake in IDZ
Water Management (WC/WDM, losses, billing, credit control)
Historic
Water use
Years

## Slide 56
Future Water Requirement Scenarios
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Scenario | Water requirement component |  |  |  |  |  |  | 
 | Current industries (fixed & variable) | New identified IDZ industries | Further new industries (% additional growth) | Municipal Urban/ domestic (% growth) | Increased domestic supply in Mhlatuze catchment (% growth) | Increased domestic supply: Mtubatuba Scheme | Irrigation | WC/WDM (% saving on current use; phased in over 10 yrs.)
Sc 1: Low growth |  | 25% | 0% | 1% | 1% | No |  | 0%
Sc 2: Low-Medium growth |  | 50% | 0.5% | 1% | 2% | No |  | 0%
Sc 3: Medium growth |  | 75% | 1% | 2% | 3% | Yes |  | 0%
Sc 4: High growth |  | 100% | 2% | 3.5% | 4% | Yes |  | 0%
Sc 5: Water Efficient |  | 75% | 1% | 2% | 3% | Yes |  | Urban: 15% Industrial: 10%
Discuss Table 3.4 on page 20 of Workshop BID

## Slide 57
Findings
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
IDZ expansion
IDZ expansion
Interval between old Tronox/ RBM mines closing and new mines commencing

## Slide 58
Way Forward
Source further information needed
Refine some water requirements following the workshop
Update scenarios as agreed
Write draft report & disseminate for comment
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 59: - Thank you -

## Slide 60
Additional Slides

## Slide 61: Locality Map of the City of uMhlathuze Municipality
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 62
Water Efficiency (cntd)
Foskor
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Utilize storm water captured on their own sites for their two phosphoric acid plants (1800m3 month)
They also utilize storm water from BHP Billiton (Hillside) to reduce their municipal raw water uptake
Foskor are developing their own water reduction and efficiency plan for implementation

## Slide 63
Water Efficiency (cntd)
Mondi
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Mondi implemented a program from 2005 which included a targeted reduction in their fresh water consumption by approximately 15,000m3 per day.
A Water Reduction Task Team monitors water consumption against targets set within the Mill and attempts to remedy over-use

## Slide 64
Water Efficiency (cntd)
Richards Bay Coal Terminal (RBTC)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
RBCT’s Environmental Systems Upgrade Project (ESUP) was commissioned in 2009
Storm water and water collected from the coal stockpiles is channeled into settling ponds
This recycled water is used for suppression of dust
Their overall consumption of potable reduced by 75% (2010-2012)

## Slide 65
Water Efficiency (cntd)
Richards Bay Minerals (RBM)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
Awarded first place by the DWA at the WC/WDM Sector Awards 2013
RBM invested in reducing freshwater abstraction & improving both water recycling and efficiency of use
Process water from smelting and processing activities is re-used at the mine
Their Water Management Plan identifies improved storm and process water capturing; expansion of their water treatment plant; and addressing water efficiency of tails stacking operations

## Slide 66
Water Efficiency (cntd)
The Industrial Development Zone (IDZ)
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY
The Environmental Management Framework for the Port Expansion and the IDZ recognizes the need to ensure that appropriate demand-side management measures are implemented during the development of the IDZ
It also has a strong focus though design requirements on the protection of water quality, both aquatic and marine

## Slide 67
Type of Use | User | Water Quality | Treatment Works | Source | Supplier
Industrial | Bayside Aluminium | Raw |  | Lake Mzingazi | City of uMhlathuze
 |  | Potable | Mzingazi WTW | Lake Mzingazi | City of uMhlathuze
 | Hillside Aluminium | Potable | Mzingazi WTW | Lake Mzingazi | City of uMhlathuze
 | RBCT | Potable | Mzingazi WTW | Lake Mzingazi | City of uMhlathuze
 | Tongaat-Hulett and Mondi Felixton | Potable Raw | Tongaat Hulett WTW | Lake Cubhu Mhlathuze River | City of uMhlathuze
 | Mondi | Potable | Nsezi WTW | Lake Nsezi and Mhlathuze Weir | Mhlathuze Water
 | Foskor | Clarified | Nsezi WTW | Lake Nsezi and Mhlathuze Weir | Mhlathuze Water
 |  | Potable | Mzingazi WTW | Lake Mzingazi | 
 | Tronox (Hillendale) | Raw |  | Mhlathuze Weir | Mhlathuze Water
 | RBM | Raw |  | Lake Nsezi | Mhlathuze Water
 |  | Raw |  | Mfolozi River | RBM
 |  | Raw |  | Lake Nhlabane | RBM
Domestic | Richards Bay | Potable | Mzingazi TW | Lake Mzingazi | City of uMhlathuze
 | Richards Bay (supplementary supply) | Potable | Nsezi TW | Lake Nsezi and Mhlathuze Weir | Mhlathuze Water
 | Empangeni | Potable | Nsezi TW | Lake Nsezi and Mhlathuze Weir | Mhlathuze Water
 | Nseleni | Potable | Mzingazi TW | Lake Mzingazi | City of uMhlathuze
 | Esikhaleni, Felixton and Vulindlela | Potable | Esikhaleni TW | Lake Cubhu | City of uMhlathuze
 | Ngwelezane | Potable | Ngwelezane TW | Mhlathuze River | City of uMhlathuze
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY

## Slide 68
Water Requirements Workshop
RICHARDS BAY RECONCILIATION STRATEGY STUDY