## Slide 1
PRESENTATION TITLE
Presented by:
Name Surname
Directorate
Date
NOORDOEWER / VIOOLSDRIFT DAM FEASIBILITY STUDY
Presented by:
Seef Rademeyer
Department of Water and Sanitation
Date: 27 February 2018
1

## Slide 2: NOORDOEWER/VIOOLSDRIFT DAM FEASIBILITY STUDY
      Main purpose of Study:
      Feasibility Design of the Noordoewer/Vioolsdrift Dam (NVD) on Orange River between Namibia & RSA
      Purpose of Noordoewer/Vioolsdrift Dam (NVD):
      Serve as re-regulating and/or storage dam to improve water resources availability in Lower Orange River, supplying:
        Ecological water requirements (EWRs) of the Orange River and Estuary
        Domestic water requirements
        Industrial water requirements
        Mining water requirements
        Irrigation water requirements

## Slide 3
STUDY AREA
Neckartal
Dam
Windhoek
Vioolsdrift
Springbok
Keetmanshoop
Noordoewer /
Vioolsdrift Dam
site
Upington
Johannesburg
Pretoria
Welkom
Bloemhof
Dam
Vaal
Dam
Sterkfontein
Dam
Gariep
Dam
Katse Dam
Vanderkloof
Dam
Grootdraai
Dam
Polihale
Dam site
Verbeeldingskraal Dam site
Maseru
Hardap
Dam
Neckartal
Dam
Naute
Dam
STUDY AREA
Noordoewer

## Slide 4
LOWER ORANGE RIVER
NOORDOEWER
NOORDOEWER/
VIOOLSDRIFT
DAM SITE
Namibia
South Africa
4

## Slide 5: PURPOSE OF THE STUDY
      Update the water requirement projections in Orange River System
      Determine optimum site and size for NVD
      Finalise purpose and timing of NVD for re-regulation, for larger storage and/or for both in single/phased approach
      Determine timing and most appropriate development option after NVD
      Conduct feasibility study on selected NVD site and size to ensure technical, financial, operational and institutional feasibility
      Conduct Environmental Impact Assessment (EIA) to ensure environmental and social feasibility
Main study objectives

## Slide 6
B1
7
Site A3
NOORDOEWER
VIOOLSDRIFT
POSSIBLE NVD SITES
Selected for further investigation

## Slide 7: GENERAL PROJECT LAYOUT
Residential and
operational office area
Access road
NVD international
operational area border
Side spillway
NVD embankment
Flow gauging weir
Namibia border
post
RSA border
post
N7
C13
Orange River
Vioolsdrift
B1
B1
NAMIBIA
RSA
Noordoewer
Hydropower house
NVD international
operational area border
NVD area border

## Slide 8: OPTIMUM NOORDOEWER/VIOOLSDRIFT DAM SIZE
Alternative dam development options
Vanderkloof
Dam
Gariep
Dam
Verbeeldingskraal Dam
Noordoewer/
Vioolsdrift Dam
Estuary
4
2
3
5
Vanderkloof
Dam
Gariep
Dam
Noordoewer/
Vioolsdrift Dam
Estuary
4
2
3
5
95 m / 2 117 million m 3
41 m / 645 million m 3
73.5 m / 2 800 million m³
Option 1
Option 2
Fish River
Fish River
Vaal River
Vaal River
LHWP-1
Polihali
Dam
LHWP-1
Polihali
Dam

## Slide 9
AREA TO BE INUNDATED BY OPTION 1
Option 1
95 km
Witbank
Goodhouse
Noordoewer
Vioolsdrift
Haib River
Henkries
absrtaction
Area to be inundated = 122 km2
FSL/area
inundated
9

## Slide 10
AREA TO BE INUNDATED BY OPTION 2
Option 2
50 km
Witbank
Goodhouse
Noordoewer
Vioolsdrift
Haib River
Henkries
absrtaction
Area to be inundated = 43 km2
FSL/area
inundated
10

## Slide 11: OPTIMUM NOORDOEWER/VIOOLSDRIFT DAM SIZE
Option | Option 1 | Option 2
Implementation/commissioning | 2024 | 2024
NVD height to full supply level (FSL) | 70.0 m | 41.5 m
NVD capacity | 2 800 million m3 | 645 million m3
Yield benefit @ 2024 | 666 million m3/a | 408 million m3/a
Implementation date of next scheme (Verbeeldingskraal Dam) | 2045 (21 years after NVD) | 2032* (8 years after NVD)
Benefit-cost ratio (6% discount rate) | 1.34 | 1.50
Hydropower generation at NVD | 17 MWc | 8 MWc
Additional hydropower generation in ORS | 12 MWc | 50 MWc
Alternative dam development options
* No feasibility study conducted yet for Verbeeldingskraal Dam

## Slide 12: OPTIMUM NOORDOEWER/VIOOLSDRIFT DAM SIZE
  Verbeeldingskraal Dam
      To implement will take about 15 years to go through feasibility (including assessment of EWRs), design and construction phases
      Separate EIA process required
      Flooding of Lesotho area – negotiation period
      Raise capital for 2 large dams
      Cost apportionment negotiations with Namibia for all dams
      URV for Verbeeldingskraal Dam is lower than raising of Gariep Dam
Other practical considerations

## Slide 13: CONCLUSIONS
  Study to be finalised regarding the best option (NVD size) for implementation
  Engagement currently underway between South Africa and Namibia on the optimum development option
  EIA to be conducted as per chosen best development option

## Slide 14: .
THANK YOU