## Slide 1: CLASSIFICATION OF SIGNIFICANT WATER RESOURCES AND DETERMINATION OF RESOURCE QUALITY OBJECTIVES FOR WATER RESOURCES IN THE USUTU TO MHLATHUZE CATCHMENTS (WP11387)
8.5 ECOSYSTEM SERVICES: CONSEQUENCES OF SCENARIOS

## Slide 2
ECOSYSTEMS SERVICES:
SCENARIO ANALYSIS
Greg Huggins

## Slide 3: OVERVIEW
Natural habitats and ecosystems provide a range of environmental goods and services.
River systems and their associated use values are of particular importance.
This study followed the approach of the 2005 Millennium Ecosystem Assessment and classifies ecosystem services as follows:
  Provisioning, e.g. fish, riparian veg, sand winning, stock-watering.
  regulating, e.g. waste assimilation/dilution, flood attenuation, bank protection.
  cultural, e.g. ritual and recreational use.
  supporting services, e.g. biomass production, nutrient cycling.

## Slide 4: METHOD
The value of eco-system services to riverine and estuarine systems was examined – see Status Quo Report.
The profile of ecosystem services associated with each site was determined, keeping in mind they represent a wider area, and thereafter assessed against the planning scenarios applicable to the site.
A list of the relevant ecosystem services that were found in the various reaches examined, and deemed to be significant, was generated as a table. These were cross checked with the biophysical experts that formed part of the project team.

## Slide 5
Rivers Goods & Services

## Slide 6
Estuaries Goods & Services

## Slide 7: METHOD
The biophysical specialists then identified the potential change, against a normative value expressed as “1”, that each of the key ecosystem services may undergo in each of the scenario clusters. The potential change was noted as a factor and used in later calculations. For example, no change = 1, a 50% increase = 1.5, and a 20% decrease = 0.8.

## Slide 8: METHOD
Scenario impacts amalgamated into provisioning, regulating, cultural, and supporting services categories.
Scenarios are weighted for the importance of the services at each EWR site. For example, where regulating services are significant, it will be given a higher weight.
All weightings are normalised against a base score of 1. Where all four services are deemed to be of equal importance then a score of 0.25 would be allocated to each.
Example: Matigulu River; CC scenario
Service |  | Weight
Provsioning Services (P) | 1.023 | 0.4
Regulating Services (R) | 0.950 | 0.2
Cultural Services (C) | 1.000 | 0.3
Supporting Services (S) | 1.000 | 0.1
Weighted Score | 0.999 | 1

## Slide 9: RIVER RESULTS: SUMMARY
Nseleni – note impact can be >1, e.g. where conditions favour some species (rip veg) change that have Provisioning Services importance.
All rivers:
  Results fluctuate between 0.954 and 1.043
  Scenarios show little impact on Ecosystem Services

## Slide 10: ESTUARY RESULTS
Scenarios:
1. Climate change
2. Reduction of present day MAR by 15%
3. Increase of present day MAR by 15%
 | 1 | 2 | 3
Provisioning Services | 0.50 | 0.67 | 1.33
Regulating Services | 0.93 | 0.94 | 1.04
Cultural Services | 0.73 | 0.80 | 1.16
Supporting Services | 0.64 | 0.74 | 1.19
Weighted Score | 0.67 | 0.77 | 1.21
Most estuaries: No significant changes under scenarios
Examples: Siyaya

## Slide 11
Scenarios:
1. Climate Change
2. Present Day including EWR releases from Lake Nhlabane
3. Increase MAR + 15%
4. Restoration Scenario to allow for mouth breaching each year. Increase of flows with interventions – significant positive increase driven by fish species availability
 | 1 | 2 | 3 | 4
Provisioning Services | 0.78 | 1.00 | 1.02 | 3.84
Regulating Services | 1.01 | 1.00 | 1.00 | 0.70
Cultural Services | 0.88 | 1.00 | 1.14 | 3.22
Supporting Services | 0.88 | 0.99 | 1.17 | 1.40
Weighted Score | 0.86 | 1.00 | 1.07 | 2.78
iNhlabane

## Slide 12
Scenarios:
1. Climate change
2. Present day including the upgrade of the Mtunzini WWTW
3. Present day – additional 10% demand on MAR supplied by Eshowe Dam with an increased capacity of 15 million m3.
4. Similar to above – with 10% increase abstraction from lower reaches
5. Present day reduced by 20% through abstraction from lower reaches of river
6. Present day reduced by including additional demand of 10% on present day MAR supplied by Eshowe Dam. Maximum Development
 | 1 | 2 | 3 | 4 | 5 | 6
Provisioning Services | 0.68 | 0.60 | 0.96 | 0.89 | 0.71 | 0.68
Regulating Services | 0.76 | 0.82 | 0.98 | 0.90 | 0.84 | 0.81
Cultural Services | 0.76 | 0.71 | 0.96 | 0.93 | 0.81 | 0.78
Supporting Services | 0.68 | 0.74 | 0.97 | 0.86 | 0.72 | 0.68
Weighted Score | 0.72 | 0.69 | 0.96 | 0.90 | 0.77 | 0.74
uMlalazi