## Slide 1
Description of Operational Scenarios
Presented by:
Stephen Mallory
IWR Water Resources
17 March 2014

## Slide 2
NWRCS integrated steps
1: Delineate units of analysis and describe the status quo
2: Initiation of stakeholder process and catchment visioning
3: Quantify EWRs and changes in Ecosystem Services
7: Gazette class configuration
4: Identification and evaluation of scenarios within IWRM
5: Draft Management Classes
6: Resource Quality Objectives (EcoSpecs & water quality (user))
Scenarios: Where does it fit in?

## Slide 3
Scenarios
Scope of this presentation
  What is a scenario?
  Presentation of preliminary scenarios
Purpose
  This presentation together with the discussion document are intended to stimulate debate and allow stakeholders to suggest additional scenarios

## Slide 4: What is a scenario?
Scenarios
A scenario is a plausible definition (or setting) of all the factors (variables) that influence the water balance and water quality in a catchment and the system as a whole.
Scenarios are used to assess different levels of water use and protection with the aim of finding a balance between ecological protection and utilisation of the resource.
In essence, water resource classification is the process of evaluating scenarios and recommending the preferred (after stakeholder consultation) scenario for implementation.

## Slide 5: Preliminary Scenarios: Komati
Natural
  No water use, only natural flows. This sets the baseline upon which all other scenarios are built.
Present Day
  The situation as currently understood taking into account all known water users and operating rules.
Revised Present Day
  The Verification process currently being undertaken by the ICMA will shortly produce updated water use estimates. The water resources models will be updated with this information.
Scenarios

## Slide 6
Include ecological water requirements (REC)
  The REC ecological water requirements will be included as a priority water requirement (in addition to the Revised Present Day water use)
Future water use
  This scenario will allow for increased water use in the catchment based on the following data sources:
    Komati Basin Treaty
    All Towns Reconciliation Study
    Interim IncoMaputo Agreement
  This future water use scenario will be modelled with the REC and PES ecological water requirements included.
Scenarios

## Slide 7
    Uptake of unutilised demands
      There is approximately 14.8 million m3/annum of allocated to irrigators but currently unutilised water in the upper Komati. The Department of Rural Development and Land Affairs (DARDLA) are planning to reinstate this irrigation, some of which could be located downstream of Swaziland.
    Impact of mining operations on the water quality in the upper Komati
      This scenario will consider the impact of uncontrolled mining development with eventual acid mine drainage.
      This could be modelled with and without transfers of water from the Usuthu catchment.
Scenarios

## Slide 8
Scenarios
Summary
Scenario | Scenario Variables |  |  |  |  | 
 | Update water demands | Domestic growth and increase irrigation | EWR1 | IIMA4 Flows | DARDLA | Mining
K1 | Yes | No | No | No | No | No
K2 | Yes | No | Yes (REC3) | No | No | No
K3 | Yes | Yes | Yes (PES2) | Yes | No | No
K4 | Yes | Yes | Yes (REC) | Yes | No | No
K5 | Yes | Yes | To be decided | Yes | Yes | No
K6 | Yes | Yes | To be decided | Yes | To be decided | Yes

## Slide 9: Preliminary Scenarios: Crocodile
Natural
  No water use, only natural flows. This sets the baseline upon which all other scenarios are built.
Present Day
  The situation as currently understood taking into account all known water users and operating rules.
Revised Present Day
  The Verification process currently being undertaken by the ICMA will shortly produce updated water use estimates. The water resources models will be updated with this information.
Scenarios

## Slide 10
Include ecological water requirements (REC)
  The REC ecological water requirements will be included as a priority water requirement (in addition to the Revised Present Day water use)
Future water use
  This scenario will allow for increased water use as obtained from the following sources:
    All Town Reconciliation Strategies
    Mbombela Reconciliation Strategies
  Increased cross border flow in terms of the Interim IncoMaputo Agreement will be included in this strategy
  This scenario will be modelled with the REC and PES ecological water requirements.
Scenarios

## Slide 11
Mountain View Dam
  This scenario will include Mountain View Dam on the Kaap River.
  This scenario will be modelled with and without ecological water requirements
Boschkejskop Dam
  This scenario will include Boschjeskop Dam on the Kaap River.
Scenarios

## Slide 12
Scenarios
Summary
Scenario | Scenario Variables |  |  |  |  | 
 | Update water demands | Domestic growth | EWR | IIMA Flows | Boschjeskop Dam | Mountain View Dam
C1 | Yes | No | No | No | No | No
C2 | Yes | No | Yes (REC) | No | No | No
C3 | Yes | Yes | Yes (PES) | Yes | No | No
C4 | Yes | Yes | Yes (REC) | Yes | No | No
C5 | Yes | Yes | No | Yes | No | Yes
C6 | Yes | Yes | To be decided | Yes | No | Yes
C7 | Yes | Yes | To be decided | Yes | Yes | ?

## Slide 13: Preliminary Scenarios: Sabie
Natural
  No water use, only natural flows. This sets the baseline upon which all other scenarios are built.
Present Day
  The situation as currently understood taking into account all known water users and operating rules.
Revised Present Day
  The Verification process currently being undertaken by the ICMA will shortly produce updated water use estimates. The water resources models will be updated with this information.
Scenarios

## Slide 14
Include ecological water requirements (REC)
  The REC ecological water requirements will be included as a priority water requirement
Future water use
  This scenario will allow for increased water use for the increased domestic requirements for Mbombela and possible increased irrigation for emerging farmers.
  This scenario will be modelled with the REC and PES ecological water requirements.
Scenarios

## Slide 15
Future water use: Increased forestry in the Sand River catchment
  This scenario will allow for increased afforestation in the upper reaches of the catchment as proposed by the Department of Agriculture and Forestry.
New Forest Dam
  This scenario will include New Forest Dam on a tributary of the Sand River.
Scenarios

## Slide 16
Scenarios
Summary
Scenario | Scenario variables |  |  |  | 
 | Update water demands | Growth in water demands | EWR | Reinstate Sand Forestry | New dam at New Forest (Sand River)
S1 | Yes | No | No | No | No
S2 | Yes | No | Yes (REC) | No | No
S3 | Yes | Yes | Yes (REC) | No | No
S4 | Yes | Yes | To be decided | Yes | No
S5 | Yes | Yes | To be decided | To be decided | Yes