## Slide 1
PRESENTATION TITLE
Presented by:
Name Surname
Directorate
Date
DETERMINATION OF WATER RESOURCE CLASSES AND RESOURCE QUALITY OBJECTIVES FOR THE WATER RESOURCES IN THE MZIMVUBU CATCHMENT
Defining System Operating Rules
Training, 31 May
Colin Talanda

## Slide 2
1. Background
2. Creating a representative Network
3. Using “penalties” to define operating rules
Contents

## Slide 3
1. Background

## Slide 4
Operation of system must be controlled
Generally based on:
  Practical experience
  Specialist analysis
Overall objectives:
  Optimise utilisation of water resource
  Minimise cost of operation
General

## Slide 5
Typical aspects
Prioritisation of supply to water users
Prioritisation of use of water sources
Conditions under which inter-reservoir and inter-basin support occurs (i.e. Ntabaleng & Laleni)
EWR Requirements (i.e Laleni Hydropower operation)
Minimisation of spillage
Blending options
Flood management

## Slide 6
Selection process
Define objectives (scenario matrix)
Select initial set of operating rules
Implement initial selection in model
Undertake analysis and interpret results
Evaluate achievement of objectives
Reselect operating rules
Repeat selection process

## Slide 7
Selection process

## Slide 8
2. Creating a representative network model

## Slide 9
Reservoir
Identify main physical features
Irrigation
Recreation
Urban
Industrial
Ecology
Runoff
Water source
Water users
River

## Slide 10
X
X
X
= Reservoir
= Runoff
= Flow route (with sink )
= Junction node
= Water user
X
Representative model symbols

## Slide 11
Resulting network model
2
Urban
Industrial
Irrigation
3
3
5
7
4
1
6
2
Ecology
Recreation
4
1

## Slide 12
Demands/Water Use
Urban/Industrial: 12 monthly values (monthly distribution)
Irrigation: Irrigation blocks i.e. Allocation, irrigation efficiency, return flow, soil characteristics, effective rainfall factors, evaporation, crop types/crop factors, irrigation area

## Slide 13
Demands/Water Use
Afforestation and Alien Invasive: Time series from Hydrological Analysis
Ecological Water Requirements (EWRs): Range of monthly runoff reference flows & Real Monthly IFR flows (corresponding to reference flows)
(show file from Drew)

## Slide 14
3. Using “penalties” to define operating rules

## Slide 15
Tool for implementing selected operating rules in model
Dimensionless value assigned by analyst to system components:
  Channels: for every unit of flow
  Reservoirs: for every unit of water in storage
Interpreted by comparing relative size
Basis of model flow-routing solution
Penalties

## Slide 16
Penalty selection (1 of 3)
Flow = 0 m3/s
Flow = 2 m3/s
Flow = 2 m3/s
User
Flow
P = 10
2 m3/s P = 5
User
Flow
P = 10
2 m3/s P = 11
User
Flow
P = 1
2 m3/s P = 5

## Slide 17
Flow 1 = 0 m3/s
Flow 2 = 2 m3/s
Flow 1 = 0 m3/s
Flow 2 = 0 m3/s
Flow 1 = 2 m3/s
Flow 2 = 2 m3/s
Penalty selection (2 of 3)
Flow 1
User 1
Flow 2
User 2
P = 20
2 m3/s P = 15
2 m3/s P = 5
Flow 1
User 1
Flow 2
User 2
P = 10
2 m3/s P = 15
2 m3/s P = 5
Flow 1
User 1
Flow 2
User 2
2 m3/s P = 15
2 m3/s P = 5
P = 1

## Slide 18
Flow 1 = 2 m3/s
Flow 2 = 0 m3/s
Flow 3 = 2 m3/s
Flow 1 = 0 m3/s
Flow 2 = 2 m3/s
Flow 3 = 2 m3/s
Penalty selection (3 of 3)
User
B
Flow 1
A
Flow 3
Flow 2
P = 1
P = 10
2 m3/s P = 5
User
B
Flow 1
A
Flow 3
Flow 2
P = 1
P = 10
2 m3/s P = 5

## Slide 19
Reservoir
Irrigation
Recreation
Urban
Industrial
Ecology
Runoff
Water resource system
11.5
30 m3/s (Pri. 8)
(Pri. 5)
(Pri. 4)
(Pri. 1)
10 m3/s
1 m3/s
0.5 m3/s
21.0
(Pri. 7)
(Pri. 6)
20 m3/s
1 m3/s
4 m3/s (Pri. 3)
1 m3/s (Pri. 2)

## Slide 20
Network model with penalties
2
Urban
Industrial
Irrigation
3
1
4
Ecology
Recreation
P = 1
P = 10
P = 100
P = 400
P = 1000
11.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
3
5
4
2
7
6
1

## Slide 21
2
Urban
Industrial
Irrigation
3
3
5
4
4
2
Ecology
Recreation
7
6
P = 1
P = 10
P = 100
P = 400
P = 1000
11.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
Case 1: Reservoir in Zone 1
Water level
1
= channel flow in m3/s
1.0
37.5
16.5
5.0
11.5
21.0
4.0
16.5
1

## Slide 22
2
Urban
Industrial
Irrigation
3
3
5
4
4
2
Ecology
Recreation
7
6
P = 1
P = 10
P = 100
P = 400
P = 1000
11.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
Water level
= channel flow in m3/s
1.0
17.5
16.5
5.0
11.5
1.0
4.0
16.5
1
1
Case 2: Reservoir in Zone 10

## Slide 23
2
Urban
Industrial
Irrigation
3
3
5
4
4
2
Ecology
Recreation
7
6
P = 1
P = 10
P = 100
P = 400
P = 1000
1.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
Water level
= channel flow in m3/s
1.0
6.5
6.5
5.0
1.5
0.0
4.0
16.5
1
1
Case 3: Reservoir in Zone 100

## Slide 24
2
Urban
Industrial
Irrigation
3
3
5
4
4
2
Ecology
Recreation
7
6
P = 1
P = 10
P = 100
P = 400
P = 1000
0.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
Water level
= channel flow in m3/s
1.0
5.5
5.5
5.0
0.5
0.0
4.0
16.5
1
1
Case 4: Reservoir in Zone 400

## Slide 25
2
Urban
Industrial
Irrigation
3
3
5
4
4
2
Ecology
Recreation
7
6
P = 1
P = 10
P = 100
P = 400
P = 1000
0.5
30 m3/s P = 2
P = 20
P = 200
P = 1200
10 m3/s
1 m3/s
0.5 m3/s
21.0
P = 5
P = 15
20 m3/s
1 m3/s
4 m3/s P = 500
1 m3/s P = 750
Water level
= channel flow in m3/s
0.0
0.5
0.5
0.0
0.5
0.0
0.0
16.5
1
1
Case 5: Reservoir in Zone 1000

## Slide 26
Basic building blocks: “arcs”
Allow particular flows under specific
circumstances
For each arc, 3 data values defined:
  Lower flow limit
  Upper flow limit
  Penalty (“dis-benefit” of every unit of flow)
Up to 5 arcs, generally only 1 or 2
Modelling channel penalties

## Slide 27
1-arc channel
Flow = 0 to X; Penalty = P
D/s node
U/s node
Configuration
Arc
0 to X
P
Standard notation

## Slide 28
D/s node
U/s node
Configuration
Arc 2
Arc 1
Flow = 0 to X; Penalty = P
Flow = X to Y (usually Y = X); Penalty = 0 (usually)
Standard notation
0 to X
P
X to Y
0
2-arc channel (1 of 2)

## Slide 29
2-arc channel (2 of 2)
2
Urban
Industrial
Irrigation
3
1
4
Ecology
Recreation
4 m3/s P = 500
6
500
0 to 4
0
4 to 4
6

## Slide 30
Defined in terms of “storage zones” and
“rule curve level”
For each zone, 2 data values defined:
  Elevation of lower zone boundary
  Zone penalty
Penalty relation to rule curve:
  Above: “dis-benefit” of water in storage
  Below: “benefit” of water in storage
Modelling reservoir penalties

## Slide 31
Standard reservoir notation
P3 (50)
P2 (10)
P4 (10 000)
P1 (-1 000)
Bottom
DSL
FSL
Zone level
Rule curve level

## Slide 32
35
33
34
YIELD
20
0 to inf.
53
10
0 to Inf.
46
2
0 to 5.0
52
0
0 to inf.
50
10
35
1303.00 (FSL)
1287.00 (DSL)
2
20
33
1548.96 (FSL)
1533.00 (DSL)
1547.99 (90 %)
47
250
0 to 0.13
0
0.13 to 0.13
45
200
0 to TD
0
TD to TD
54
250
0 to 0.64
0
0.64 to 0.64
Heyshope Dam
Grootdraai Dam
50
45
52
53
54
46
47
Compensation
Spill
Compensation
Spill
Example: Heyshope-Grootdraai transfer (2 of 2)

## Slide 33
4. Practical 2: Interpreting penalties

## Slide 34
Purpose:
Explore use of penalties to model operating rules
Investigate behaviour of system under various situations
Methodology:
Analyse system for 3 cases
Complete table with results
Purpose and methodology

## Slide 35
Physical system
Irrigation
Urban
Reservoir B
Reservoir A
Transfer
Reservoir B
Ecology
Ecology
Natural runoff
Natural runoff

## Slide 36
2
Urban
Irrigation
3
1
A
6
Network model with penalties
B
20
A
1
10
5
0 – 2
4
50
0 to 1.0
0
1.0 to 1.0
2
5
0 to 10
0
10 to 10
B
7
Ecology
50
0 to 2.0
0
2.0 to 2.0
5
Ecology
30
0 to 2.0
0
2.0 to 2.0
3

## Slide 37
2
Urban
Irrigation
3
1
A
6
B
A
10
5
0 – 2
4
50
0 to 1.0
0
1.0 to 1.0
2
5
0 to 10
0
10 to 10
B
7
Ecology
50
0 to 2.0
0
2.0 to 2.0
5
Ecology
30
0 to 2.0
0
2.0 to 2.0
3
Case 1: Reservoir A in Zone 1
20
1

## Slide 38
2
Urban
Irrigation
3
1
A
6
B
A
5
0 – 2
4
50
0 to 1.0
0
1.0 to 1.0
2
5
0 to 10
0
10 to 10
B
7
Ecology
50
0 to 2.0
0
2.0 to 2.0
5
Ecology
30
0 to 2.0
0
2.0 to 2.0
3
20
10
1
Case 2: Reservoir A in Zone 10

## Slide 39
2
Urban
Irrigation
3
1
A
6
B
A
5
0 – 2
4
50
0 to 1.0
0
1.0 to 1.0
2
5
0 to 10
0
10 to 10
B
7
Ecology
50
0 to 2.0
0
2.0 to 2.0
5
Ecology
30
0 to 2.0
0
2.0 to 2.0
3
20
10
1
Case 3: Reservoir A fails

## Slide 40
Case 1: Reservoir A in zone 1
Channel No.
Flow (m3/s)
Case 2: Reservoir A in zone 10
Channel No.
Flow (m3/s)
Case 3: Reservoir A failure
Channel No.
Flow (m3/s)
Table to be completed:
Channel
Flow in channels for indicated cases
7
7
7
6
6
6
5
5
5
4
4
4
3
3
3
2
2
2
1
1
1

## Slide 41
Results

## Slide 42
Completed table:
Case 1: Reservoir A in zone 1
Channel No.
Flow (m3/s)
Case 2: Reservoir A in zone 10
Channel No.
Flow (m3/s)
Case 3: Reservoir A failure
Channel No.
Flow (m3/s)
Channel
Flow in channels for indicated cases
7
2
7
2
7
2
6
0
6
0
6
2
5
2
5
2
5
1
4
1
4
1
4
1
3
3
3
3
3
2
2
10
2
0
2
0
1
13
1
3
1
2

## Slide 43
End
DWS TRAINING