## Slide 1
The Determination of Water Resources Classes and Resource Quality Objectives for the water resources in in the Breede-Gouritz WMA
Focus on Breede-Overberg area
Technical Task Group meeting 2: Presentation and workshopping of draft Resource Quality Objectives
Rivers
Presented by: Karl Reinecke
12-16 March 2018
Graham & Rhona Beck Skills Centre, Robertson

## Slide 2
Co-ordinate implementation of the Water Resources Classification System (WRCS):
  Determine Water Resources Classes (WRCs)
  Determine Resource Quality Objectives (RQOs)
  Support Gazetting of Recommended Water Resources Classes and RQOs
  for the water resources in the Breede-Gouritz WMA:
  - Rivers - Estuaries - Groundwater
  - Dams - Wetlands
Study Objectives

## Slide 3
Overview of Study Progress

## Slide 4: Classification and RQOs Steps
7-step process to determine WRCs
7-step process to determine RQOs
Gazette WRC & RQO
Aligned

## Slide 5: Defined Integrated Units of Analysis (IUAs)
  Identified significant resources:
    Based on Physical, Biological & Socio-economic factors
  Each IUA represents a similar area requiring a Water Resources Class (WRC)
  Why do we need these?
    Broad-scale units to assess socio-economic implications of scenarios (possible future situations)
    Report on ecological conditions at a sub-catchment scale
    Set WR Classes for different parts of a catchment
  18 IUAs delineated - 10 in the Breede-Overberg & 8 in the Gouritz-Coastal areas

## Slide 6
18 Integrated Units of Analysis

## Slide 7: Defined Resource Units (RUs) and Nodes
  Nodes are locations of interest (points) in a water resource (rivers, dams, wetlands, estuaries)
  Are sited using:
  Water infrastructure
  Aquatic ecosystem attributes
  Are used to allocate water for environment and development
Resource units (RUs) are grouped areas e.g. river basins, deemed similar in terms of various characteristics
Are used to transfer information between catchments
Groundwater

## Slide 8
Integrated Units of Analysis and Nodes
Breede-Overberg Region

## Slide 9
Integrated Units of Analysis and Nodes
Gouritz-Coastal Region

## Slide 10
Gouritz-Coastal Region
 | Integrated Unit of Analysis (IUA) |  | Recommended Classes
 | Gamka Buffels | C6 | II
 | Touws | E8 | III
 | Gouritz-Olifants | D7 | III
 | Lower Gouritz | F13 | II
 | Duiwenhoks | F12 | III
 | Hessequa | I18 | III
 | Groot Brak | G14 | III
 | Coastal | G15 | II

## Slide 11
Complete
Complete
Study Status: RQOs
Draft
Draft
Draft
DAMS
DAMS
Notes: Erik to present progress, Reminder of two stage process (Classification followed be RQOs – but gazetted together). Link to RQOs? Then zoom in on the classification process

## Slide 12
Three RQO Reports disseminated for comment:
  Resource Unit Prioritisation Report
  Evaluation of Resource Units Report
  Outline of RQOs Report
Please provide comment by 22 March to:
  Esther Lekalake (LekalakeE@dws.gov.za), or
  Louise Lodenkemper (Louise.Lodenkemper@aurecongroup.com)
Comments on draft RQO Reports

## Slide 13: Thank you, Any discussion?

## Slide 14
Determination of RQOs
Notes: Erik and team to present the methodology used for scenario evaluation

## Slide 15: Terminology
Ecological Reserve studies – set flow quality and quantity for water resource condition and basic human needs
  Ecological Water Requirement (EWR) sites
Classification – determines condition classes I – III
  Integrated Units of Analysis (IUA)
Resource Quality Objectives – descriptive (words) and numerical (number) statements to measure resource quality
Resource Units – rivers, lakes, wetlands, groundwater

## Slide 16: Steps to RQOs
IUAs - a combination of socio-economic and biotic boundaries
RUs for rivers were quaternary catchments
  RUs were prioritised
  RUs were evaluated
  RQOs were written
Notes: Part of the purpose is to try focus attention at all the areas of the basin that differ from one another…to be representative as a whole across the basin

## Slide 17: Resource Unit priorities - method
2 levels of ranking RUs at a quaternary level
  Quats with nodes were selected first as these were chosen based on a range of biophysical, water resource and socio-economic reasons
  The ‘DWS RU prioritisation tool’ was used to rank RUs against one another based on:
    position, socio-economic and international importance
    role in regulating services and ecological importance
    management actions needed or taking place
Notes: Management only looks at nodes in poor condition and then EWR sites

## Slide 18: High and low priority RUs

## Slide 19: High priority RUs

## Slide 20: Evaluation of RUs - method
The ‘DWS RU evaluation tool’ was used to select indicators for which RQOs (descriptive and numerical) were written based on:
  Activities that impact on the water resource
    Dams, IBTs, afforestation, agriculture and so on
  User requirements
    Conservation and ecosystem characteristics (including PES, trajectory of change)
    Industry, agriculture, ecotourism, real estate (including fitness for use and trajectory of change)
Notes: Evaluation of Rus method statement

## Slide 21: Examples of indicators
Hydrology - low flows and high flows, monthly average volume (MCM)
Ecological condition – IHI, PAI, GAI, VEGRAI, MIRAI, FRAI
Geomorphology – sediment particle size (D50)
Aquatic and riparian vegetation - % cover of indigenous and alien cover in 3 zones
Macroinvertebrates – SASS and ASPT scores, # of families present, key indicator families
Fish – CPUE of fish species present, FROC
Notes: RQOs method statement

## Slide 22: RQOs - method
TEC was the REC scenario
20 high priority RUs in the Gouritz (9) and Outeniqua (11)
  Descriptive RQOs, numerical limits and TPCs
40 Gouritz River nodes and 32 Outeniqua nodes
  Hydrological and ecological condition RQOs
Notes: RQOs method statement

## Slide 23: Gouritz and Outeniqua RQOs – low priority
Target Ecological Condition from the REC scenario
Monthly average volume (MCM) that include inter-annual floods (return period > 2 years)
Annual volume (MCM) – sum of months
%nMAR – annual flow as a % of natural

## Slide 24: Gouritz River basin RQOs – high priority
2 different sets
Gouritz River Reserve study
  E.g. GOUR_DORI_J12L
Other
  E.g. GOUR_GROO_J11J
Notes: DRAFT RQOs

## Slide 25: Outeniqua RQOs – high priority
2 different sets
Groot Brak Reserve study
  E.g. OUTE_GROO_K10E
Knysna River study
  E.g. OUTE_DIEP_K40A
Notes: DRAFT RQOs

## Slide 26: Doring River @ GOUR_DORI_J12L

## Slide 27: Doring River @ GOUR_DORI_J12L
Flow
Excludes inter-annual floods

## Slide 28: Doring River @ GOUR_DORI_J12L
Water quality

## Slide 29: Doring River @ GOUR_DORI_J12L

## Slide 30: Doring River @ GOUR_DORI_J12L

## Slide 31: Doring River @ GOUR_DORI_J12L

## Slide 32: Groot River @ GOUR_GROO_J11J

## Slide 33: Groot River @ GOUR_GROO_J11J
Flow
Excludes inter-annual floods

## Slide 34: Groot River @ GOUR_GROO_J11J
Water quality

## Slide 35: Groot Brak River @ OUTE_GROO_K10E

## Slide 36: Groot Brak River @ OUTE_GROO_K10E
Flow
Excludes inter-annual floods

## Slide 37: Groot Brak River @ OUTE_GROO_K10E
Water quality

## Slide 38: Groot Brak River @ OUTE_GROO_K10E

## Slide 39: Groot Brak River @ OUTE_GROO_K10E

## Slide 40: Groot Brak River @ OUTE_GROO_K10E

## Slide 41: Diep River @ OUTE_DIEP_K40A

## Slide 42: Diep River @ OUTE_DIEP_K40A
Flow
Excludes inter-annual floods

## Slide 43: Diep River @ OUTE_DIEP_K40A
Water quality

## Slide 44: Diep River @ OUTE_DIEP_K40A

## Slide 45: Diep River @ OUTE_DIEP_K40A

## Slide 46: Diep River @ OUTE_DIEP_K40A

## Slide 47: SWA, FEPAs and protected areas
FEPAs, CBAs, ESAs
SWA, where current day > 70% of natural
Rivers important for fish conservation
Table of quaternary and/or coordinate taking note of these areas but not writing RQOs specifically – double edged sword?
Will not be gazetted but part of the RQO document