## Slide 1
EXISITNG OPERATING RULES OF MAJOR DAMS BUILT INTO WATER RESOURCES YIELD MODEL FOR THE LETABA RIVER SYSTEM
31 October 2013
INFORMATION WORK SESSION
Presented by:
Pieter van Rooyen

## Slide 2: Major Dams focussed on
Dap Naude
Ebenezer
Magoebaskloof & Vergelegin
Hans Merensky
Tzaneen
Thabina
Middel Letaba
Nsami
Modjaji

## Slide 3: Location of Dams on Map

## Slide 4: Location of Dams on Map

## Slide 5: Location of Dams on schematic diagram: Upper Letaba 1
Dap Naude
Ebenezer
Georges Valley Canal
Pusela Canal

## Slide 6
Location of Dams on schematic diagram: Upper Letaba 2
Magoebaskloof
Vergelegin
Hans Merensky
Tzaneen
Thabina
Noord Canal
NN Canal

## Slide 7: Location of Dams on schematic diagram: Middle Letaba
Middel Letaba
Nsami
Canal

## Slide 8: Location of Dams on schematic diagram: Lower Groot Letaba
Modjaji

## Slide 9: DAP NAUDE
Current court order: 0.028 m3/s released from November to June, with the full inflow to the dam being released in August, September & October
Present day simulated 0.028 m3/s all year round
No support to Ebenezer
Current abstraction: Polokwane: 4.07 mill m3/a (gauge: B8R006)
Present Day simulated
Court order

## Slide 10: EBENEZER
Rule: no support to Tzaneen BUT reality shows different
2 release events from Ebenezer when
Tzaneen Dam low

## Slide 11: EBENEZER
To simulate closer to observed, built in rule to support Tzaneen when Tzaneen drops below 15%
Tzaneen
Ebenezer
With support to Tzaneen
No support to Tzaneen
Tzaneen
Ebenezer

## Slide 12: EBENEZER DEMANDS & RESTRICTIONS
Directly from dam: Polokwane: 16.2 million m3/a (Gauge B8R001)
Irrigation:
    Releases for Georges Valley Canal: 2.54 million m3/a
    Releases for Pusela Canal: 7.00 million m3/a
    Releases for Main stem: 1.85 million m3/a
    Total: 11.4 million m3/a
Irrigators restricted based on Tzaneen Dam operating rule and levels AND 0 allocation when Ebenezer < 20%
Urban 70% allocation when Ebenezer < 20%

## Slide 13: MAGOEBASKLOOF & VERGELEGIN
Measured canal outflow from Magoebaskloof, 4.6 million m3/a (gauge: B8R003)
Irrigation for tea plantation greatly reduced from allocation for present day run
Abstraction from Vergelegin for Industry and town = 2.16 million m3/a, given priority
Magoebaskloof
Vergelegin

## Slide 14: HANS MERENSKY
No support to Tzaneen
Only irrigation demand from dam, 4.5 million m3/a

## Slide 15: TZANEEN DEMANDS AND RULE
Rule: below 95% irrigators cut to 50% allocation, reviewed incrementally as dam recovers above 95%
Below 15% irrigators get 0%, urban cut to 70%
Irrigation:
    Noord Kanaal: 28.8 million m3/a
    N&N Kanaal: 13.03 million m3/a
    Main River Tzaneen: 27.85 million m3/a
    Total: 69.68 million m3/a
0.6 m3/s must pass Letaba Ranch, released from Tzaneen when incremental insufficient
Urban demands: Tzaneen town, Ritivi 1 & 2, Ba Phalaborwa: 12.4 million m3/a

## Slide 16: Tzaneen Dam simulated
With restriction rule
No restriction rule

## Slide 17: MIDDEL LETABA
Releases through canal to Nsami Dam as per measurements (gauge B8R007) 18.3 million m3/a
Abstraction and losses from canal calculated from measurements (gauge B8R007 - B8H067): 16.8 million m3/a
Urban abstraction from dam: 2.7 million m3/a

## Slide 18: NSAMI
Urban abstraction from dam: 2.8 million m3/a

## Slide 19: MODJADJI
Urban abstraction from dam: 2.9 million m3/a

## Slide 20: THABINA
Urban abstraction from dam: 2.8 million m3/a